## Slide 1: GHHD Annual Report
European Centre
“Geodynamical Hazards of High Dams”of the Council of Europe

## Slide 2: Operating Automatic Early Warning Telemetric System for Dam Diagnostics DAMWATCH COUNCIL OF EUROPE EUR-OPA MAJOR HAZARD AGREEMENT, EUROPEAN CENTRE “GEODYNAMICAL HAZARDS OF HIGH DAMS” GEORGIA, TBILISI M.Nodia Institute of Geophysics, 1 Alexidze str. – Tbilisi 0171 – Georgia; Phone: (995 32) 33 28 67; E-mail: tamaz.chelidze@gmail.com “ALGO Ltd” (Tbilisi) The system is permanently operating for 14 years
Enguri Dam International Test Area -EDITA (Western Georgia)
Diagnostic Centre
Internet
GSM net
Sensors+Controllers in the dam body and foundation
GSM modem
tiltmeters
T
The cost effective early warning/monitoring telemetric system DAMWATCH transfers in real time the data on tilts and other geotechnical parameters of dam body to the diagnostic center in order to compare observed tilts with theoretical values at given water load and in case of approaching the theoretical limit critical values to issue a warning for dam administration.
T
12 years long time series of tilts of Enguri high arc dam. Hysteresis in tilt records during lake load-unload points to nonlinear elasticity of dam body, probably caused by cracks and joints.
T
Tilt time series from April 2010 to June 2010 (sampling 1 minute). Note short-term variations in dam tilts (arrows); this means that it is possible to feel and diagnose the finest deformation of dam body.
Scheme of Automatic Early Warning Telemetric system DAMWATCH
Tiltmeter
“Applied
Geomechanics”
Results of diagnostics of the tilt time series from April 2010 to June 2010 by nonlinear analysis tool –Recurrence Quantification Analysis RQA (% of determinism); note clear anomalies at perturbations
Geodynamical Monitoring system at EDITA
T
T
T
T
T
Tiltmeters
T
T
T
Laser strainmeter

## Slide 3: Development of innovative cost-effective autonomous telemetric early warning system for detecting floods, mudflows and rockfall initiation (2016-2017 project)
The concept
Parameters
Sensors
Low-power source
Collecting/Processing/Diagnostic Board
Transmission
Analysis/Decision Making
The suggested debris flow/landslide EWS network includes monitoring of two main factors, leading to mass-movement: humidity of the soil (as a relatively long-term precursor) and displacement/acceleration/acoustics caused by initiation of mechanical motion (as a short-term precursor).

## Slide 4: Multi-sensor (humidity, tilts, acceleration - left) in hermetic box, the array of sensors and processing box.

## Slide 5: Monitoring/Early Warning System “Watchdog” (landslides, mudflows): Assembled field version for remote control: 1- Rod post 2- Solar batteries 3 – Processing block 4 - Sensors 5 – Transmitting block with ARDUINO and GPS antenna 6 - Server of the Monitoring system
1
2
3
4
5
6

## Slide 6: Block scheme of EWS “Watchdog”
Gldani landslide area
Google image of Gldani landslide area
Sensors

## Slide 7: Real-time EWS data of x, y acceleration components, tilts t, humidity h, power e
 | id | created at | logic | x | z | t | h | e
0 | 1 | 2018-10-11 11:49:27.297000+00:00 | 0000 | 59 | 93 | 171 | 3873 | 4592
1 | 2 | 2018-10-11 11:49:27.299000+00:00 | 0000 | 59 | 103 | 166 | 3883 | 4567
2 | 3 | 2018-10-11 11:49:27.300000+00:00 | 0000 | 73 | 88 | 181 | 3873 | 4587
3 | 4 | 2018-10-11 11:49:27.300000+00:00 | 0000 | 59 | 83 | 171 | 3873 | 4577
4 | 5 | 2018-10-11 11:49:27.300000+00:00 | 0000 | 68 | 98 | 161 | 3883 | 4592
5 | 6 | 2018-10-11 11:49:27.301000+00:00 | 0000 | 68 | 83 | 161 | 3873 | 4582
6 | 7 | 2018-10-11 11:49:27.301000+00:00 | 0000 | 68 | 83 | 152 | 3883 | 4582
7 | 8 | 2018-10-11 11:49:27.302000+00:00 | 0000 | 64 | 88 | 176 | 3878 | 4562
8 | 9 | 2018-10-11 11:49:27.302000+00:00 | 0000 | 64 | 93 | 176 | 3883 | 4582
9 | 10 | 2018-10-11 11:49:27.302000+00:00 | 0000 | 83 | 98 | 176 | 3878 | 4587
10 | 11 | 2018-10-11 11:49:27.303000+00:00 | 0000 | 108 | 103 | 186 | 3873 | 4582
11 | 12 | 2018-10-11 11:49:27.303000+00:00 | 0000 | 73 | 98 | 186 | 3873 | 4587
12 | 13 | 2018-10-11 11:49:27.303000+00:00 | 0000 | 68 | 117 | 171 | 3878 | 4597
13 | 14 | 2018-10-11 11:49:27.304000+00:00 | 0000 | 68 | 103 | 176 | 3873 | 4572
14 | 15 | 2018-10-11 11:49:27.304000+00:00 | 0000 | 83 | 103 | 171 | 3883 | 4582
15 | 16 | 2018-10-11 11:49:27.304000+00:00 | 0000 | 68 | 88 | 176 | 3878 | 4582
16 | 17 | 2018-10-11 11:49:27.305000+00:00 | 0000 | 59 | 103 | 166 | 3873 | 4592
17 | 18 | 2018-10-11 11:49:27.305000+00:00 | 0000 | 78 | 93 | 161 | 3883 | 4567
18 | 19 | 2018-10-11 11:49:27.305000+00:00 | 0000 | 59 | 88 | 181 | 3878 | 4582
19 | 20 | 2018-10-11 11:49:27.306000+00:00 | 0000 | 64 | 93 | 161 | 3873 | 4587
20 | 21 | 2018-10-11 11:50:15.787000+00:00 | 0000 | 73 | 103 | 186 | 3883 | 4592
21 | 22 | 2018-10-11 11:50:15.788000+00:00 | 0000 | 59 | 93 | 171 | 3878 | 4572
22 | 23 | 2018-10-11 11:50:15.788000+00:00 | 0000 | 68 | 98 | 176 | 3873 | 4592
23 | 24 | 2018-10-11 11:50:15.788000+00:00 | 0000 | 73 | 103 | 171 | 3878 | 4587
24 | 25 | 2018-10-11 11:50:15.788000+00:00 | 0000 | 59 | 98 | 161 | 3878 | 4592
25 | 26 | 2018-10-11 11:50:15.789000+00:00 | 0000 | 68 | 64 | 127 | 3888 | 4357
26 | 27 | 2018-10-11 11:50:15.789000+00:00 | 0000 | 68 | 93 | 176 | 3873 | 4465
27 | 28 | 2018-10-11 11:50:15.789000+00:00 | 0000 | 73 | 93 | 176 | 3878 | 4597
28 | 29 | 2018-10-11 11:50:15.789000+00:00 | 0000 | 88 | 88 | 166 | 3878 | 4597
29 | 30 | 2018-10-11 11:50:15.789000+00:00 | 0000 | 64 | 93 | 171 | 3883 | 4597
30 | 31 | 2018-10-11 11:50:15.790000+00:00 | 0000 | 68 | 93 | 176 | 3873 | 4592
31 | 32 | 2018-10-11 11:50:15.790000+00:00 | 0000 | 64 | 93 | 166 | 3878 | 4597
32 | 33 | 2018-10-11 11:50:15.790000+00:00 | 0000 | 49 | 98 | 156 | 3873 | 4587
33 | 34 | 2018-10-11 11:50:58.149000+00:00 | 0000 | 73 | 103 | 186 | 3883 | 4592
Chart: X - 10/10/2018; 15:45-21:L42
Chart: Z - 10/10/2018; 15:45-21:42
Chart: T - 10/10/2018; 15:45-21:42
Chart: H - 10/10/2018; 15:45-21:42
humidity

## Slide 8
Development of effective and cost-effective telemetric autonomous EWS is very important, especially for developing countries, which are most vulnerable to Hydro-geological catastrophes. Creation of such systems became possible last years thanks to development of compact, precise and very cheap high-tech devices
-------------------------------------------------------------------------------------------------
Only Set-up costs for Flood Forecasting System developed in Ireland ( www.environment-agency.gov.uk) costs €120,000.
---------------------------------------------------------------------------------------------------------------------------------------------------------------------------------
A catastrophic flashflood/mudflow occurred in the Vere River valley in Tbilisi, the capital of Georgia, on the night of 13 to 14 June 2015 as a result of heavy shower, which lasted 2.5-3 hours (precipitation - 50 cm). It resulted in at least 22 human deaths, economic losses more than 20 million $. It struck the Tbilisi Zoo, leaving half of its animal inhabitants either dead or on the loose. The sequence of events represents a classic cascading sequence of heavy rainfall, slope failure, catastrophic flashflood, landslides, roads' blockage, wild animals wandering on the streets of capital city. The Vere river is characterized by periodic flash floods, which had turned this normally small stream into a surging river, causing significant flooding in 1960, 1963, 1972, and 1995.
Development of innovative cost-effective autonomous telemetric early warning system for detecting floods, mudflows and rockfall initiation (2018-2019) with CERG

## Slide 10: Wild animals wandering on the streets of capital city

## Slide 11
2018 (GHHD)
Specific objectives
WP1. Analysis of existing water level monitoring systems' sensors for selection of modern cost-effective and accurate sensors for monitoring water level in rivers
WP2. Assembling and testing the water level monitoring prototype module including sensors and data acquisition system and testing it in laboratory conditions.
WP3. Assembling and testing of existing cost-effective power sources (solar batteries etc) to provide autonomous regime of water level monitoring system in rivers in laboratory conditions.
Expected Results
WP.1. Selection of modern cost-effective and accurate sensors for monitoring water level in rivers
WP.2. Assembled and tested in laboratory conditions monitoring prototype module for water levels in rivers
WP.3. Assembled and tested in laboratory conditions cost-effective power sources
Deliverables
i. Operating water level monitoring/early warning system prototype module including sensors and data acquisition system for detecting flood initiation tested in laboratory conditions
ii. Cost-effective power source (with solar panel, batteries etc) to provide autonomous regime of water level monitoring system in rivers in laboratory conditions

## Slide 12: Ultrasonic Distance Sensor Module JSN-SR04T measures with mm accuracy the distance from 0.25 to 9 meters.
 | Features small size, easy to use low voltage, low power consumption high accuracy strong anti-jamming integrated with wire enclosed waterproof probe, suitable for wet, harsh measurement occasions Specification Working voltage: DC 5V Static working current: 5mA Working current: 30mA Acoustic emission frequency:40KHz Wiring:+5V(positive); Trig(control); Echo(receive); GND(cathode); Application Horizontal distance messurement Obstacle avoidance, automatic control Traffic control Security, industrial control
Sensor: For continuous measurement of WL of the river we connect the super-sensitive distance meter sensor JSN-SR04T to the platform Arduino mega 2560. The sensor measures with high accuracy the distance to the object (here WL in the river) in the range of 0.25 – 9 m. Numerous experiments show that sensor measures the distance in this range with accuracy of one millimeter.

## Slide 13: Data acquisition system: for monitoring of water level in rivers in the real time we use processing-diagnostic-remote transmitting block - Arduino Mega 2560.For continuous transmission of WL data we use the mobile Internet system, as the use of cable Internet is not appropriate. Exactly, we use the SIMCOM SIM900 Module Quad Band Wireless GSM/GPRS Shield, which is matched to our main platform and can be easily manipulated. Besides, the system is energy-conserving and stable in exploitation.
 | 1. Quad-Band 850/ 900/ 1800/ 1900 MHz 2. GPRS multi-slot class 10/8 3. GPRS mobile station class B 4. Compliant to GSM phase 2/2+ Class 4 (2 W (AT) 850/ 900 MHz) Class 1 (1 W( AT) 1800/1900MHz) 5. Control via AT commands (GSM 07.07 ,07.05 and SIMCOM enhanced AT Commands) 6. Short message service 7. Free serial port selection 8. All SIM900 pins breakout 9. RTC supported with SuperCap 10. Operation temperature: -40 ~ +85 Specifications: PCB size:71.4mm X 66.0mm X 1.6mm Indicators:PWR, status LED, net status LED Power supply:9~20V, compatible with Arduino Communication Protocol:UART RoSH:Ye Application Ideas M2M (Machine 2 Machine) Applicatoions. Remote control of appliances. Remote Weather station or a Wireless Sensor Network. Vehicle Tracking System with a GPS module.

## Slide 14: Memory system: In order to guarantee the stable operation of WL monitoring system a memory card will be connected to the main platform (Arduino mega 2560) using Micro SD (TF) Storage Board with 16 GB flash memory card. This warrants uninterrupted recording of WL data from the distance meter. Micro SD card slot Supports SDIO and SPI interfaces 2.54 mm pitch pinheaders

## Slide 15
Software Routine
Into ARDUINO memory the following code written in C is booted
The program’s main body is
// main.c
// *=================================
// * Libraries
// *==================================
#include <Time.h>
#include <TimeLib.h>
#define
TINY_GSM_MODEM_SIM900
#include <TinyGsmClient.h>
#include <TinyGsmClientSIM800.h>
#include <TinyGsmCommon.h>
#include <TinyGsmFifo.h>
#include <ArduinoHttpClient.h>
#include <TimerOne.h>
#include <SD.h>
// *=================================
// * Global state variables
// *==================================
String deviceName = "E"; // Name
time_t currentFileTime = 0;
// Last time file name was changed
String currentFileName = "";
// Current file name, blank by default
time_t alarmAt = 0;
// Alarm started at
time_t sendFileTime = 0;
// Last time file were sent
int sendFileEvery = 0;
// Send file every seconds
// *=================================
// * Local libraries
// *==================================
#include "configuration.h"
#include "error.h"
#include "sensors.h"
#include "modem.h"
#include "storage.h"
#include "setup.h"
void loop() {
storageSetCurrentFileName();
storageWrite();
storageFlush();
delay(1000L);

## Slide 16: Power source (solar panel, batteries) We use the system of powerful (150 W) mono-crystal solar battery for long duration of power source, lithium-ferro-polymer accumulators, automatic charging module for fast charging of accumulators
Solar battery RPG-150W(Vmp-17,64V,
Imp-8,51A,Voc-21,60V, Isc-9,53A
Rechargeable Batteries 12 V 10Ah LiFEPO4 SLA - Dakota Lithium with discharge graph (red)
LTC3780 10A DC 5V-32V to 1V-30V Automatic Step Up Down Regulator Charging Module
The assembled power charging module with accumulators
The assembled double hermetized power charging module

## Slide 17
The assembled EWS for flood was tested in laboratory conditions just during visit of Gianluca Silvestrini to Georgia. The system operates normally.
In 2019 we plan to arrange telemetry and test the system in the Vere river valley, where the June 2015 catastrophe occurred.