## Slide 1
Session 1.4
Computer & Internet Basics
Xxxxx XXXXXXXX
Council of Europe
email
DD Month YYYY
Introductory Judicial Training Course on Cybercrime and Electronic Evidence
Notes: This session is 90 minutes in length

## Slide 2
Session contents
Computer parts & functions
Internet parts & how it came to be
Connecting to the internet
Internet services & applications
Deep web, anonymity & the Dark Web
Notes: This session is going to be split into 5 parts to provide natural breaks.
Idea is to describe what a computer is – or a device capable of connecting to the internet which all have similarities
The to describe what the internet is and how it works
And then to look at how that computer connects to the internet
And then look at what is out on the internet itself

## Slide 3
Session aim
Provide information about technology that will be encountered by Judges and Prosecutors during their work and which is used:
by criminals to commit crime and
by law enforcement to detect it.
The aim is to enable the audience to gain sufficient knowledge about technology for them to function more effectively in their roles.
Notes: This aim is a very wide one – and the aim is to provide an informative overview without dropping into a highly technical description
The forensic analyst’s job is to take a very complicated subject and make it simple – whilst retaining the knowledge that computers are highly complex devices

## Slide 4
Session objectives
By the end of the session, delegates will be able to:
Recognise the common components of a computer system & understand their role;
Describe what the internet is, how someone connects to it & what possible traces can be left in doing so;
List some internet services & applications which may they may encounter in their role as prosecutors & judges;
Give examples of issues the dark web could bring to criminal prosecution.
Notes: This session is going to be split into 5 parts to provide natural breaks.
Idea is to describe what a computer is – or a device capable of connecting to the internet which all have similarities
The to describe what the internet is and how it works
And then to look at how that computer connects to the internet
And then look at what is out on the internet itself

## Slide 5: Computer parts & functions
Computer & Internet Basics
Section 1
5

## Slide 6
Famous last words
“There will never be a market for more than 5 computers in the world”. Thomas Watson - Chairman of IBM – 1943
“There will never be a reason anyone would want a computer in their home”. Ken Olson, Founder of DEC – 1977
“A PC will never need more than 640K of memory”. Bill Gates - Founder of Microsoft - 1981
Notes: The purpose of this slide is to show that even the most technology literate people could not have envisaged the changes that technology would bring. The delegates are not alone in perhaps not understanding the impact that technology has on their role and the quotes on this slide may encourage them to believe that technology in the criminal justice system should not be feared but embraced with all the necessary safeguards in place.

## Slide 7
Computer systems
Notes: No matter what device we encounter – they all have similarities.
There is likely to be a screen to be able to see what the device is doing and get some output
There will be some way to input data into the device – such as a keyboard or mouse – or a touchscreen to interact
The device will have some temporary storage (memory) which allows it to save data
It will have a processor which will allow it compute
It will have some more permanent storage
It will have the ability to have things connected to it to interact
It will probably need to connect to a network
It needs power to work
To try to explain the working parts of a device, we will make an assumption that they have similarities – so we can understand what they do

## Slide 8
Common to devices
Hardware
Software
Notes: All of our devices will have some form of hardware & some software to allow the user to interact with the device
Hardware are the physical bits we can see and touch
Software are the programs that run on the hardware
The largest piece of software on a computer system is likely to be the Operating System

## Slide 9
Hardware
Going to deal with one type of device and apply the logic to other types of devices
Notes: Impossible to break down every device in the time allowed and discuss everything – so important to try to put a context on this and describe basic principles of how a computing device works

## Slide 10
Case/Housing
Notes: This is a base desktop. We will build a theoretic computer basing it on such a machine.
We have to be aware that the principles of all other devices are very similar. The components exist across the board
We will start nice & simple – we need you all to understand what we are doing here & building a device from nothing & looking at what all the parts of it do
The blue box is our case & we are going to populate it

## Slide 11
Power supply
PSU
Notes: Supplies electrical current to different parts of the computer – offering different voltages for areas as required
The Power Supply Unit (PSU) in a computer regulates and delivers the power to the components housed in the case. Standard power supplies turn the incoming 110V or 220V AC (Alternating Current) into various DC (Direct Current) voltages suitable for powering the computer's components. Power supplies have a certain power output specified in Watts, a standard power supply would typically be able to deliver around 350 Watts. The more components there are in a PC the greater the power required from the power supply.
Different standards – standard kettle lead input for a computer, different tip for smaller devices, batteries for portable devices
Modular, Hybrid, non-modular

## Slide 12
Motherboard/PCB
PSU
‘If this were a human, it would be our ‘central nervous system’ – everything links into it & allows communication between all the main parts’
Notes: PCB – Printed Circuit Board
The motherboard is like our own central nervous system – everything links into it
A motherboard is also known as the main board or system board of the computer. The motherboard is the central circuit board of a computer. All other components and peripherals plug into it.
The job of the motherboard is to relay information between them all. The motherboard houses the BIOS (Basic Input/Output System), which is the simple software run by a computer when initially turned on.
Other components attach directly to it, such as the memory, CPU (Central Processing Unit), graphics card, sound card, hard-drive, disk drives, along with various external ports and peripherals.
Top two images are computer motherboards – bottom one is from an iPhone – same principle – just different sizes of components

## Slide 13
Motherboard
Holds system information
CMOS – Complimentary Metal Oxide Semiconductor – stores date/time/boot information
Battery retains data when system is off
BIOS – Basic Input Output System
Base system to get computer running before handing to main operating system
BIOS being phased out for UEFI – Unified Extensible Firmware Interface
Notes: Mother board has many components - and many ways to connect to it
CMOS and BIOS - CMOS and BIOS are often used interchangeably; you can think of the BIOS as software, and CMOS as the hardware running it.
Abbreviated from Complementary Metal Oxide Semiconductor, CMOS is usually pronounced "see-moss". CMOS is the hardware in a computer that performs very low-level functions and very basic computer start routines.
Newer computers use the Unified Extensible Firmware Interface (UEFI) instead of a BIOS
UEFI is a specification that defines a software interface between an operating system and platform firmware.
UEFI replaces the Basic Input/Output System (BIOS) firmware interface originally present in all IBM PC-compatible personal computers

## Slide 14
Buses
Communication system that transfers data between components inside a computing device
Notes: The rear of the board often allows us to see the different ‘buses’ that are used within a system. There are many different types – allowing data to move around the system at differing speeds
Most commonly known bus – USB! Universal Serial Bus
This is the rear of the PCB for a Samsung Galaxy where you can clearly see the bus tracks

## Slide 15
CPU
PSU
CPU
Takes instruction from RAM
Performs calculations
Processes data
Delivers output back to RAM
Notes: The central processing unit – CPU – performs calculations, actions and allows programs to run. Takes instruction – decodes & processes – delivers an output
Top graphic – Intel Core i7 chip
Middle graphic – Apple A13 chip from 2020 iPhones
Bottom graphic – Cooling fan. Processors generate large amounts of heat & need to disperse these so manufacturers come up with ways of keeping them cool – especially difficult in smaller devices (phones, etc) which have to be manufactured differently to stop heat generation

## Slide 16
RAM/Memory
PSU
CPU
Volatile storage
Holds device’s ‘work in progress’
Very fast storage
Works alongside CPU
Can contain useful data *
RAM
Notes: The memory is the working area of a device. RAM is generally much faster than other storage allowing it to work well with the CPU. All running programs are loaded to memory & run from there. The operating system is also loaded into memory
* Can be read when the system is running – in cybercrime cases where exploits are performed by an attacker, the content of memory can be vital. Will deal with this later

## Slide 17
Video/Graphics Card
PSU
CPU
Allows computer information to be seen/read
Can be built in to motherboard or added as independent, bespoke device
GPU – Graphics Processing Unit
RAM
c
GPU
Notes: Graphics show two different types of bespoke video cards.
The video/graphics card or unit allows some form of visual output to a screen or monitor. Almost every computer system needs to show data to the user – whether a computer or a phone. Some graphics units are designed for speed & refreshing – such as gamer type devices where graphics are key. Other devices simply have a screen to be able to interact – the graphic module turns data into visible information
Can have their own processor and RAM – the higher the specification
Some mother boards have graphics built in
In older computer modelling, everything mentioned so far would form parts of the ‘North Bridge’ – faster performing devices within a system

## Slide 18
Hard drive/storage
PSU
CPU
More permanent storage
Holds operating system, programs & user files when system is off
Probably the most useful part of the device evidentially
RAM
Hard Disk(s)
GPU
Notes: Top graphic – exposed revolving disk
Middle graphic – exposed solid state drive
Bottom graphic – iPhone 6 16GB Toshiba memory chip
Top is the traditional storage – bottom becoming more common. Bottom is faster due to the technology
All devices will have permanent storage which is the key to many investigations – capturing & analysing the content

## Slide 19
Network
PSU
CPU
RAM
Hard Disk(s)
GPU
Allows connectivity out of device
Necessary for Internet access
Often called NIC – Network Interface Cord (or controller)
Has unique identifier – MAC (Media Access Control) address
Network Card
Notes: Top graphic – fixed RJ45 network card
Middle graphic – Wifi card for PC
Bottom graphic - Wifi Antennae for mobile device (iPhone)
All devices that need to communicate require some form of network connectivity
Network Interface Controller (NIC) – is a circuit board or card installed into a computer that allows it to connect to a network
Media Access Control (MAC) address – is a quasi-unique identifier assigned to most network adapters or network interface cards (NICs) by the manufacturer for identification and which provides a unique value.

## Slide 20
www.coe.int/cybercrime
PCI/PCI Express/USB
PSU
CPU
RAM
Hard Disk(s)
GPU
Network Card
Allow expansion or upgrade of system
Adding components like storage or input devices
PCI
USB
Notes: Top graphic – PCI & PCI Express slots
Middle graphic – USB ports on side of a laptop
Bottom graphic – Keyboard & mouse – connected to the system by USB wireless dongle
A computer system on it’s own can function but it does need external devices or components to be trying ‘networked’

## Slide 21
Audio/video/storage
PSU
CPU
RAM
Hard Disk(s)
GPU
Network Card
PCI
USB
Allow input/output to & from system
Added removable storage
Audio
Video
Storage
Notes: Top graphics – audio connections & HDMI for video connection to other devices – TV, monitor, screen
Middle graphic – DVD drive
Bottom graphic – MicroSD card added to phone to increase storage capacity
All devices that need to communicate require some form of network connectivity
All of these have identifiers known as MAC addresses – Media Access Control number

## Slide 22
Computer systems
Notes: This is a repeat of the opening slide – but we need to emphasise that each of these devices has commonality with the concepts shown previously in this section - they just look different in each

## Slide 23
Evidence sources in devices
Disks
Removeable storage
Memory
Notes: From the previous slides, need to emphasise that we are looking at these three areas as sources of digital evidence from computers, phones and other computing devices
The internal permanent storage of a hard drive
What can be added as temporary removeable storage such as USB devices, DVD or SD cards
The internal volatile storage of RAM

## Slide 24
Disks
Normally one - but can be multiple (servers, CCTV, etc)
  Spinning disks or solid state disks
Some modern devices have non-removeable storage
  Giving added complication to investigators
IDE, SATA, mSATA, M.2 & U.2 formats
Notes: Hard Disk Drives - Most computers have at least one hard disk and many have more. Larger computers such as mainframes will typically have many hard disks. It is now common for other devices such as CCTV and music players to also have hard disks which can hold huge amounts of data. These disks have hard platters on which information is held and data can be easily deleted and rewritten, while the structure of the disk is remembered, making them viable for long periods of time. Data is stored on the surface of a platter in sectors and tracks. Tracks are concentric circles of data sectors, and sectors groups of bytes (512 or 4096) stored together. Data is stored on hard disks as files which are simply a group of “bytes”. Programmes are also files and these are also called by the CPU in order to be used.
SSD storage devices bring new challenges to digital forensics examiners as the data is stored in a completely different way.

## Slide 25
Removeable storage
CD/DVD technology still seen but diminishing
USB devices
  External hard drives
  ‘Thumb’ drives
SD & MicroSD media cards
  Likely cameras & phones
Notes: CD/DVD/Blu-Ray Disks – These disks may hold varying amount of data and are typically used to store music, video or computer files for distribution. A DVD for example is the same size as a CD and holds about 7 times as much data as a CD. A Blu-Ray disk, which may be used to store high definition content in turn currently holds more than 10 times as much as a DVD. In other words they can store more data than was possible on a hard disk only a few years ago. They all store data in a different way than hard disks and the data held on them is not as volatile as that stored on hard disks.

## Slide 26
Computing devices/computer systems
Digital Cameras
Drones
GPS
Wearables
VR Glasses
Notes: This slide adds devices that are less obvious perhaps as computing devices – but nevertheless are just that with characteristics similar to the one we theoretically built
Each of these devices have the same characteristics as computer systems mentioned previously – internal storage, connection to the outside world, ability to input to them, ability to get information from them
That information is made more difficult through the large number of different ways that devices store their data – some on flash memory, some on hard drives, some on memory cards, some on solid state storage. This is carried forward into the next slide.
For example, many printers today have non-volatile storage where they collate the information they are going to print – before actually printing it. These data files could be of use if recovered and analysed. Similarly, a digital camera or a GPS will have its own internal memory as well as a removeable memory card. The need is to consider both of these together. Drones have internal memory storage which may tell where they were and when.
And wearables are computer systems in their own right – acting in many cases in the same way a connected digital phone might do.

## Slide 27
www.coe.int/cybercrime
Computer systems
Notes: This slide adds devices that are less obvious perhaps as computing devices – but nevertheless are just that with characteristics similar to the one we theoretically built
Whilst we have developed ways of dealing with the more common devices such as desktops, laptops, mobile phones, etc. the way we deal with lesser known or less popular devices does mean sometimes there is no ‘bespoke’ solution – and one has to be created in a way that what is recovered is understandable, believable and done to a standard.
Imagine a murder where the investigator wanted to know what time the lights came on (and which ones), when the last time the air conditioning came on, was the emergency button pushed and which one and what does the CCTV hold – the answer is in the computer system(s) in the house!

## Slide 28
Computer systems
Frankie IS a computer system
‘Frankie’
Telematic unit which stores …..
eMMC memory chip
Notes: Build 1 - This is Frankie (name given to him by the investigators)! Frankie is an Audi S4 Avant 3.0l Quattro – he costs around € 40,000. He does 0-60 in 4.7seconds & has a top speed of 155mph. Frankie is (was) a nice car!
Frankie was stolen on 26 July 2018 – and was recovered 6 weeks later. He was used in a large number of thefts of cash from ATM’s – by removing the ATM physically from the wall of buildings by an organised gang in the UK who used Frankie as a getaway car.
Build 2 – Frankie IS a computer system – possibly contained in him Call logs, SMS logs, Media files (audio, video, images), Connected Devices, Contacts, Device Events, Destinations, Trackpoints (travel history), Saved travel routes, Velocity logs – lights on/off, Doors opened – gear changes, Parking lights (on or off), Odometer readings, Power events – USB added
Build 3 – Frankie has one of these – a telematic unit. This records details of almost everything that has been done involving Frankie’s computer systems, on a chip called an eMMC chip
Build 4 – an eMMC chip – which needs to be removed from the telematics unit & analysed for data using bespoke software for details of what Frankie has been up to!
And the answer was quite a lot of bad things!

## Slide 29
Mini computers
Notes: Computer systems are becoming smaller and smaller nowadays. Devices that look like USB Sticks can in reality be fully equipped computers with a processor, memory, graphics and network card and are running their own operating systems. Examples for such miniature computers are the Intel NUC, Raspberry Pi and several HDMI media sticks like Amazon FireTV, Google Chromcast, etc.

## Slide 30
Software
Operating system
  Windows, Mac, Linux, iOS, Android
  Allows hardware to communicate with the installed software
July 2020
Notes: An operating system is a software programme that allows the hardware to communicate with software programmes. Without an operating system the computer would not be able to function. There are different types of operating system depending on the type of computer or other digital device.
Most applications developed for computers are written for specific operating systems although it is now more common for them to be available for more than one platform.

## Slide 31
Software
Other software
  Productivity – office suites
  Readers & Viewers
  Archive tools
  Browsers
Notes: Top – office suite graphics – Second – Adobe, ile Viewer Plus, ACDSee – Third WinZip & WinRar – lastly browsers (of which these are the big 5 – there are many others)
There are thousands upon thousands of different pieces of software – some paid for, some free
There is software commercially written – and that which is privately developed
There is software which is legal and lawful – and there is that developed for an ulterior purpose. Many lawful pieces of software can be used for illegal purposes too
Some may be for specific operating systems and some may work on all

## Slide 32
Virtual machines
Very common to encounter
Especially in business & crime!
Ability to run a ‘Guest’ operating system within your ‘Host’ operating system

## Slide 33
Virtual machines
Processor
RAM
Graphic Card
HDD
Network Card
Mouse, Keyboard
CD/DVD
Host Operating System
Guest Operating System 1
Guest Operating System 3
Virtual Machine Manager
Hypervisor
Guest Operating System 2
Notes: This graphic describes how a virtual machine runs on a computer
The computer has HDD, Processor, Memory, graphics card, network card etc
And a HOST operating system installed on the HDD
The HOST can run – and a virtual machine manager is installed – VMWARE, Virtual Box, etc
The virtual machine software is run and a new GUEST operating system is installed – just like on a stand alone PC
But it is using the resources

## Slide 35: internet parts & how it came to be
Computer & Internet Basics
Section 2
Notes: Before we move into the internet, we need to put a little perspective on what a network is & what makes one up – which are important to allowing understanding of how the internet works

## Slide 36
Internet
Notes: Before we move into the internet, we need to put a little perspective on what a network is & what makes one up – which are important to allowing understanding of how the internet works

## Slide 37
Networks
Network terminology
IP Address – unique identifier on a network *
Port – an endpoint for network communication
  Are virtual – don’t actually exist (65,536 of them)
  Allow different applications on the same computer to utilise network resources – e.g.
    Web browsing (HTTP) Port 80
    Secure web browsing (HTTPS) Port 443
    Simple mail (SMTP) Port 25
TCP ‘Socket’ – combination of IP address plus port
Notes: * We will come back to this
Ports – idea here has to be not to confuse people which would be very easy. Concept has to be to show that on the ONE pipe coming in or out, there are virtual channels separating data of different types for different applications
Ports 0-1023 – Well Known Ports (allocated by IANA – Internet Assigned Numbers Authority)
Ports 1024 – 49151 – Registered Ports (can be registered with IANA)
Ports 49153 – 65535 – Free to be used in client programs

## Slide 38
Networks
Network hardware
Server
  Provides information or ‘services’ to other computers
Hub
  Used to connect network devices together
Switch
  Used to connect network devices together with some intelligence
Router
  Used to determine the next network point a packet should be sent so has to be connected to 2 networks
Notes: Server – is a computer or device that provides information or services to other computers on a network. Given the right software, any network connected computer can be configured as a server. In most cases, a dedicated powerful computer designed to be “always available”. One computer can run several services – e.g. web server, email server, file server, print server etc. In a business reality it often makes sense to run different services on different machines for reasons of security and to minimise the impact of any failure.
Network Hub - or concentrator is a device for connecting multiple twisted pair or fibre optic Ethernet devices together, making them act as a single network segment. Hubs work at the physical layer (layer 1) of the OSI model, and the term ‘layer 1 switch’ is often used interchangeably with hub. The device is thus a form of multi-port repeater. Network hubs are also responsible for forwarding a jam signal to all ports if it detects a collision.
Network Switch - is a computer networking device that connects network segments. In the past, it was faster to use Layer 2 techniques to switch, when only MAC addresses could be looked up in content addressable memory (CAM). With the advent of ternary CAM (TCAM), it was equally fast to look up an IP address or a MAC address.
Router - is a device that determines the next network point that a packet should be forwarded towards its destination. It must be connected to at least 2 networks. It is intelligent and works on routing tables. It is located at the gateway to a network. The term ‘layer 3 switch’ often is used interchangeably with router, but a switch is really a general term without a rigorous technical definition.

## Slide 39
Networks
Networks generally have limitations
  Number of users, building infrastructure, geographical area, etc.
  Applies to ethernet or wireless
LAN – Local Area Network
  Your home, your office, a school
WAN – Wide Area Network
  Regional, national, international
The Internet is a WAN
Notes: The trainer should ensure that information is provided to the participants that will enable them to understand the basics of networking and its limitations. They should be able to differentiate between local and wide area networks. These slides provide that basic information. Trainers should consider giving examples and encouraging participants to discuss different types of networks and how the Internet has developed. An explanation of some common relevant networking terms such as Ports and Bandwidth should be provided at this stage. Delegates should be encouraged to consider their own personal experiences; for example through their Internet access at home or at work.
LAN - A computer network covering a small geographic area, like a home, office, or group of buildings e.g. a school. The defining characteristics of LANs, include their much higher data-transfer rates, smaller geographic range, and lack of a need for leased telecom lines.
WAN - A computer network that covers a broad area (i.e., any network whose communications links cross metropolitan, regional, or national boundaries). Or, less formally, a network that uses routers and public communications links.
The largest and most well-known example of a WAN is the INTERNET.

## Slide 40
The Internet
INTERconnected NETwork
Early 1960s
Advanced Research Project Agency – for US Dept of Defence
No single point of failure – keep working in event of war/disaster
Communication continues to evolve
Notes: The term INTERNET comes from the contraction of the words INTERconnected NETwork. Many criminal activities involve the use of the Internet and this includes particular types of crime such as hacking, distribution of viruses and phishing attacks as well as more traditional crimes such as fraud. In order for Judges to effectively manage such cases that appear before them, it is necessary for them to understand the fundamentals of the Internet and its applications such as the World Wide Web and email. The following provides an introduction to the subject and provides the template for a successful training module.
The Internet began its life as the ARPANET in the 1960’s. The relevance of this information may not be immediately apparent; however, the fact that the Internet was never designed to be secure may explain why it is comparatively easy for criminals to abuse the systems. The first physical links were created in 1969 with 4 nodes being universities. The first email was sent in 1972 and the following year a new communications protocol TCP/IP was created, which now forms the basis upon which Internet communications take place. The development of the Internet as we now know it was low key in the beginning as there were disjointed separate networks, served only by limited gateways between them. This led to the application of packet switching to develop a protocol for internetworking, where multiple different networks could be joined together into a super-framework of networks.
This enabled further interconnection, which began to occur more quickly across the advanced networks of the western world, and then began to penetrate into the rest of the world. The disparity of growth between advanced nations and the developing world led to a digital divide that still exists today.
There followed the commercialisation of the Internet and the introduction of privately run Internet Service Providers in the 1980s. These enabled more popular access, which really developed in the 1990’s. The Internet has had a huge impact on commerce as well as culture. There now exists near instant communication by electronic mail (e-mail) social networking sites, text based discussion forums, and the World Wide Web. The Internet continues to grow, driven by commerce, greater amounts of online information and knowledge. The advent of Web 2.0 is upon us.

## Slide 41
Internet - brief history
4 American universities created protocols to communicate – all different for different systems
  Protocol = set of rules
1973 – early form of TCP (Stanford Uni)
  Transmission Control Protocol
1982 – TCP/IP now standard (US DoD) *
  Transmission Control Protocol/Internet Protocol
Internet Protocol – provides for IP addressing
Notes: * Will come back to this
UCLA, Stanford Research Institute, UC Santa Barbara, University of Utah – they had differing computer systems and they created different protocols – which meant that joining these up was much more difficult
1973 – a standardised protocol which meant that communication was possible
1982 – the enhancement to what we recognise today in many ways
An IP address is now a commonly used term in our work and our investigations

## Slide 42
Internet basics
Networks
Traditional communications used circuit switched – a ’circuit’ was created for communication to be completed. Break the circuit – break the communication
The internet is a packet switched network – content is broken up & makes it way to the destination
Any part fails, communication can still continue
Notes: The Internet can be thought of as the infrastructure over which many different applications can be run simultaneously. If any part of the Internet malfunctions or is destroyed, communication can still continue. No-one owns the Internet – no organisation, no corporation, no government. It is largely self regulated. It all uses the same connection technology.
Most modern data networks, like the Internet, are described as “connectionless” or “packet switched”. Traffic is split into small packets which make their own way from sender to receiver. They do not all follow the same route and are joined together again when they reach their destination.
Most people connect to the Internet through an Internet Service Provider (ISP). These are commercial organisations that rent out space. They keep records…but for how long? There are national and international legal data protection or privacy issues that impact on how long data may be retained by ISP’s. This of course has an impact on the ability of criminal justice officials to secure evidence from these sources. Connection is normally made by one of the following methods; Dial-up, Broadband (ADSL), ISDN, Cable, Wireless hotspot or Satellite.

## Slide 43
Internet basics
No one owns the internet!
There is regulation, there are rules, there is governance – which help us
Largely it is self regulated
Not everyone complies!
The internet runs on the TCP/IP protocol
Notes: The underlying principle of the Internet is that it was designed as we will see shortly, to withstand war and disaster, and still enable communication. The background to the design was military communication, and the need for it to continue in times of national emergency.
As we will go on to see later, the Internet is made up of networks of computer from all around the world, all of which can communicate easily and with resilience. Indeed someone sending an e-mail to another part of the world would probably find that the parts of that message would all go in different routes to reach the same place – and in the blink of an eye.
The Internet has evolved globally over the years – it is not owned, unlike many other computing ideas and systems, by one company. No government owns the Internet – although the US seem to take most of the responsibility for it and claim most of the success in its development. And later we will see that the French tried to legislate to stop the Internet – and failed. In fact the Afghans are the only ones we know have stopped it almost completely – by banning it in its totality.
There is no Internet police force, and although we are now trying to find ways of stopping illegality that takes place either on or through the Internet there are problems of technology and of local, national and trans-national borders and jurisdictions to overcome.

## Slide 44
Internet basics
ICANN
  Internet Corporation for Assigned Names & Numbers
  Govern domain names, IP addresses, port numbers, etc.
US Dept of Commerce
  Govern DNS root zone *
5 Regional Registries
    ARIN – North America
    RIPE – Europe, Middle East, Central Asia
    APNIC – Asia & Pacific
    LACNIC – Latin America & Caribbean
    AfriNIC – Africa (created 2004)
Governance
=
Records
=
Investigative Potential
Notes: American Registry for Internet Numbers (ARIN) for North America
Réseaux IP Européens - Network Coordination Centre (RIPE NCC) for Europe, the Middle East, and Central Asia
Asia-Pacific Network Information Centre (APNIC) for Asia and the Pacific region
Latin American and Caribbean Internet Addresses Registry (LACNIC) for Latin America and the Caribbean region
African Network Information Center (AfriNIC) was created in 2004 to manage allocations for Africa
The fact there is governance means there is investigative potential on the internet

## Slide 45
TCP/IP
TCP – Transmission Control Protocol
IP – Internet Protocol
  There are others!
Together they specify how data is exchanged on a network providing the end-to-end communication, making them reliable
TCP – creates channels, manages assembly & disassembly of packets at each end
IP – defines how to address & route each packet
Notes: We could spend days dissecting this – we will do it in one slide!
There are other protocols in the suite of protocols! Not important for our level of understanding. TCP & IP work together in Internet communication to ready data for transmission, split it up into packets, address it properly & then route it across the internet – ensuring that it reaches the destination in the way it was sent.
Therefore has built in error checking & correcting – analogy would be that a message gets split up into 10 parts – part 1 of 10, part 2 of 10, etc – and is then addressed with an IP address as it’s destination. When it gets tot eh far end, part 6 of 10 has not made it. The protocol will then identify that it has not – and request the resending of the missing part. This is done automatically and in fractions of seconds.
Some other protocols don’t do this! UDP (Universal Datagram Protocol) for example will simple break everything up and send it with no error checking. That seems ludicrous – but it is used for applications like video streaming where overheads like checking are cumbersome and the loss of a few packets in a few million are not going to be noticeable
The enormity of what is done in the background in an internet transmission is sometimes not clearly

## Slide 46
Internet protocols
HTTP – Hypertext Transfer Protocol
HTTPS – Secure HTTP
SMTP – Simple Mail Transfer Protocol
FTP – File Transfer Protocol
NNTP – Network News Transfer Protocol
UDP – User Datagram Protocol
Remember – a ‘protocol’ is simply a set of rules that if followed, allow successful communication
Notes: We could spend days dissecting this – we will do it in one slide!
There are other protocols in the suite of protocols! Not important for our level of understanding. TCP & IP work together in Internet communication to ready data for transmission, split it up into packets, address it properly & then route it across the internet – ensuring that it reaches the destination in the way it was sent.
Therefore has built in error checking & correcting – analogy would be that a message gets split up into 10 parts – part 1 of 10, part 2 of 10, etc – and is then addressed with an IP address as it’s destination. When it gets tot eh far end, part 6 of 10 has not made it. The protocol will then identify that it has not – and request the resending of the missing part. This is done automatically and in fractions of seconds.
Some other protocols don’t do this! UDP (Universal Datagram Protocol) for example will simple break everything up and send it with no error checking. That seems ludicrous – but it is used for applications like video streaming where overheads like checking are cumbersome and the loss of a few packets in a few million are not going to be noticeable
The enormity of what is done in the background in an internet transmission is sometimes not clearly

## Slide 47
IP Addresses
Every computer in a network has to have a unique ID to send & receive data – an IP address
IPv4 addresses
213.43.112.45
IPv6 addresses
2600:1403:0002:029c:0000:0000:0000:2add
IPv4 are running out – IPv6 are becoming more common as a result
Notes: IPv5 is version 5 of the IP Protocol ( Internet Protocol ) defined in 1979 and which did not transcend beyond the experimental field. It was never used as a version of the Internet Protocol .
Version number "5" in the IP header was assigned to identify packets that carried an experimental protocol, which was not IP, but ST. ST was never widely used and since version number 5 was already assigned, the new version of the IP protocol had to keep the next identifier, 6 ( IPv6 ). ST is described in RFC 1819.

## Slide 48
IPv4
32-bit address
Four numbers separated by ‘.’
Each number can be ‘0’ to ‘255’ – e.g.
213.43.112.45
4,162,314,256 possible addresses – approximately
Notes: Network/Host split defined by something called a ‘subnet mask’
Network classes – A, B & C
To do justice to this subject, the session could be hours – we will try to clear up the basics in a few slides
There are 32 bits of data reserved for the v4 IP address – which is 4 bytes of data (with 8 bits per byte)
When displayed, each byte (or octet) is split by a decimal point
A byte has 8 bits – which when stored in binary each byte has a maximum of 256 possible variations – so 0 to 255
Trying to bring in subnet masking to a basic course would be foolish – so a mention of the concept will be sufficient
Similarly there are different network classes – A, B & C – and trying to bring these in would be equally foolish at this level. If pressed, there are a maximum of 256 class A networks, each having a potential 17million + hosts; there are a maximum of 65,536 class B networks each having a potential 65,536 hosts; and there are a maximum of 17million + class C networks each with a maximum of 256 hosts. Therefore complex maths
If you worked out the maths, there could be 4.5 billion possible addresses – but the way they were subdivided in the early days in an inefficient manner means there are considerably less – which is why we are running out of them when we look at the number of devices now connected to the internet

## Slide 49
IPv4
Private v Public addresses
  Public IP addresses – used across the internet
  Private IP addresses – used in private networks
  There are certain IP address ranges that are ‘private’
Notes: Lastly you can have a private network or a public network – and there are addresses reserved for private networks
The intention is not to have the delegates remember the ranges – but to be aware they exist
Internet Assigned Numbers Authority (IANA) is the organisation responsible for registering IP address ranges to organisations and Internet Service Providers (ISPs). To allow organisations to freely assign private IP addresses, the Network Information Centre (InterNIC) has reserved certain address blocks for private use.

## Slide 50
IPv6
128-bit address – 8 values separated by colon
Values written in hexadecimal
Each group can range from ‘0000’ to ‘FFFF’ – e.g.
2600:1403:0002:029c:0000:0000:0000:2add
Can be shortened
2600:1403:2:29c:0:0:0:2add
2600:1403:2:29c::2add
340,282,366,920,938,000,000,000,000,000,000,000,000 possible
Notes: 340 undecillion - 340,282,366,920,938,000,000,000,000,000,000,000,000
“So we could assign an IPV6 address to EVERY ATOM ON THE SURFACE OF THE EARTH, and still have enough addresses left to do another 100+ earths. It isn’t remotely likely that we’ll run out of IPV6 addresses at any time in the future”
Shouldn’t need private IPs - But there is fc00:: & fdxx:xxxx:xxxx
Shouldn’t need network classes

## Slide 51
IPv6
Private v Public addresses
  As with IPv4 – same principle
  fc00:: (unique local)
  fdxx:: (site local)
  fe00:: (link local)
  Used in internal networking
Notes: Shouldn’t need private IPs - But there is fc00:: & fdxx:xxxx:xxxx
These work to allow internal networks – just like IPv4
Shouldn’t need network classes
Have subnetting – but outside the scope of this basic introductory course

## Slide 52
Your IP address (internal)
Command prompt > ipconfig /all
Notes: How do you find your internal IP address?
From the command prompt, ipconfig /all will get you this type of box – and the IPv4 & IPv6 addresses are shown
Trainer can also highlight the subnet mask!
And the MAC address – which in this case is on a wifi router (which we mentioned earlier in this section)
Much of the content here is out of the scope of this course
The trainer could do this by demonstration if they are comfortable in doing so

## Slide 53
DNS
DNS – Domain Name System
Everywhere on the internet is an IP address
123.123.123.123 (an example)
But we want to get to www.coe.int which is a URL – Uniform Resource Locator
Something has to convert www.coe.int to 123.123.123.123
DNS does this – effectively an internet telephone directory which resolves the query
Notes: Before we connect to the internet, we also need to know one very important concept – that of DNS
We are good at remembering names of things such as resources – but not so good at recalling numbers of things

## Slide 54
DNS
DNS is a multiple server system – replicated & spread out across the world
124 billion daily queries
Updated constantly
https://aws.amazon.com/es/route53/what-is-dns/
Notes: Before we connect to the internet, we also need to know one very important concept – that of DNS
We are good at remembering names of things such as resources – but not so good at recalling numbers of things
Trainer should display the graphic & talk through it for the delegates

## Slide 56: Connecting to the internet
Computer & Internet Basics
Section 3

## Slide 57
Connecting to the internet
Most people connect through an ISP (or CSP)
  Commercial organisation renting out access to the internet – 14,000+ worldwide
Common connection methods
  Dial-up, broadband, fibre, ISDN, cable, wireless hotspot, satellite
Notes: Information should be provided about how connections are made to the Internet and participants encouraged to discuss their own experiences. It should be explained that ISPs do keep records but data protection legislation restricts how long they can keep hold of them.
The role of the ISP should be explained, explaining their legal status and numbers. This is a good opportunity to discuss the importance of relationship with ISP’s in relation to accessing data and conducting lawful interception.
The simple terminology is that ISP’s rent out their access to the Internet to people – whether they are individuals or organisations.
Each ISP will keep certain information about their customers. The details and amount of it will depend on the ISP involved, and it will only last for so long – hours or days depending what is needed.
It should be possible to get –
Name, address & other info used for registration
Date registered, and how the person registered
Specific e-mail addresses or screen names unique to the user
Financial details like credit cards used to sign up to the ISP
Possibly some software detail about the user
Most importantly, detail of the history of the user’s on-line activity – dates, times & duration
TIMES ARE VITAL (Time zone issues are dealt with later in this session)
It should be pointed out that it is possible to use false details to obtain an account.
Can an ISP intercept suspect Internet traffic – YES – but depends on special equipment to record usage and monitors what is happening – so need manpower to do – costs? Also, we have to consider the authority needed to do it. In any event it is necessary to contact the ISP very early into an investigation.

## Slide 58
Connecting to the internet
ISP
Public
IP Address
Private IP Addresses
(allocated by DHCP)
Router
Router
Switch
WAP
Modem
Firewall/IDD
Private to Public swap
(done by NAT)
10.0.0.3
10.0.0.5
10.0.0.6
10.0.0.8
123.123.123.123
10.0.0.1
Notes: This build slide explains the mechanics of a standard internet connection – office, home, wireless hotspot, etc. Although not exact for everything the concept can be gained
1 Start with router
2 Two sides – the public facing & the internal facing
3 Functions of the router
4 Acts as a switch for the internal network – and its ‘route’ out – so wired & wireless
5 Router is powered on – speaks to ISP – requests an IP address
6 Means is now connected, through ISP, to the internet
7 Provided with IP address – for the router
8 9 10 11 – Devices are added to the internal network – controlled by the router’s ‘switch’ functionality
12 Router has an internal IP address – the Default Gateway (the way out)
13 14 15 16 17 – devices have their own internal/private IP addresses – allocated by DHCP – Dynamic Host Configuration Protocol
Devices can work within the network – and never have to leave it – but if they want to go out to the internet, they need to go through the default gateway – where their IP address is changed to the public IP address using NAT – Network Address Translation

## Slide 59
Bandwidth
The amount of information that can be carried through the communication line
Greater the bandwidth – faster the speed
Notes: Bandwidth – is the amount of information that can be carried through a phone line, cable line, satellite feed, and so on. The greater the bandwidth, the greater the speed of your connection and the more your Internet experience approaches a more instant-download, TV-style experience

## Slide 60
Static & Dynamic IPs
IP addresses from an ISP can be:
  Static – the same each time you connect
  Dynamic – potentially different each time
Times, dates & time zones are key in investigation
Notes: Trainer needs to ensure this is clear – a static IP address is one that stays constant. A web site needs to be at the same location on the internet each time so a web server would ideally have a static or fixed IP address.
Most ISP will allocate an IP address from a pool of addresses – so it is possible to get the same next time you connect, but more likely you will get a different one when you switch off your router.

## Slide 61
Your IP address (external)
Google ‘whatsmyip’ – many resources
Notes: How do you find your external IP address?
Do a search for anything like ‘whatsmyip’ and a host of resources will be returned
The author of these slides was in Spain when they were written – and did a look up on the IP address they were using at that time

## Slide 62
What can we learn – IP addresses
Private
  Depend on the network as to how much & how long information is retained
  Router logs
Public
  Owned/leased by a company (ISP)
  Data retention is country dependant – logging
  Requests need time, date & time zone accuracy
Notes: The public IP address is owned by a company (e.g. an Internet Service Provider (ISP))
Depending on the data retention legislation in place the ISP keeps logs about which IP address and port was assigned to which subscriber at a certain point of time.
When requesting such information from ISPs the correct IP address, port number (if available), date, time and time zone need to be provided.
The address of the subscriber does not necessarily need to be the physical location of the Internet

## Slide 63
Whois!
Can query internet databases on IP addresses & domain names – allows identification or leads for further enquiry
  Can contain registrar, registrant, dates, administrative & technical detail
  GDPR has made this less easy
Notes: Not a spelling mistake – doing a Whois on an IP address or internet resource will return a wealth of investigation data
There are countless resources for doing this – all returning potentially different information in different formats
When setting up or buying a domain, some registration and hosting information must be provided by the person/organisation doing so. There will also be payment information. This is retained by the internet governance organisations – and the hosting providers. Much used to be very accessible and publicly available – but GDPR in 2018 made it more difficult to obtain the information online and it now requires an approach to those organisations to obtain. It can be obtained but is clearly going to be a slower process now a formal request has to be made by law enforcement to obtain it.

## Slide 64
Who is 45.14.250.74?
IP Address searched
IP Address range the address comes from & some company information
Company who holds the IP address, where they are & an email – with a domain name
Some personal information about the registrant
Investigative question?
Who had the use of the IP address 45.14.250.74 at a specific time on a specific date (taking time zones into account)?
Notes: The worked example shown is for the IP address which we got as a Whatsmyip search 3 slides ago – the one being used by the author of the slide pack.
Builds - Explain when setting scene – this is a CentralOps response – but many other resources available
Trainer needs to highlight (builds)–
1 The IP address searched for
2 The range the IP address falls in – which is all held by the one company – the netname of the company & who issued it to them – RIPE
3 The company who holds the IP address – and where they are. Also an email – AND A DOMAIN – NOLIMITNET.EU
4 Some personal information about the registrant of that domain
This information collectively will answer the investigative question posed – and the answer will have to be sought from the company NO-LIMIT NETWORK using whatever means necessary to comply with jurisdictional requirements

## Slide 65
Who is nolimitnet.eu?
Notes: This is an example of having a domain name rather than an IP address. The same type of search can take place using the same internet resources. So where we had an IP address in the previous slide that took up to NO-LIMIT-NET, this is us asking the question the other way round.
Example continues – we search for the domain NOLIMITNET.EU
1 GDPR will frustrate us by not returning personal detail
2 But we will get some technical detail which can be followed up
3 Along with some information on where the network is based – and contact detail

## Slide 66
IP geolocation
IP addresses can be mapped to a physical area using geo-location services
MAY give an indication where the subscriber IP address is
Not precise – can be spoofed
This is the author’s own – and is 140 miles wrong!
All in the same region but not exact
Notes: Trainer needs to ensure that there is no misunderstanding – IP address geolocation is not accurate in many cases & will probably take an investigator down to perhaps a geographic area or a town/city – but still needs confirmation by requesting information from the ISP concerned
There are many tools to do this – all differ in how they work
Country accuracy is probably around 95-99%, region/state perhaps 55-80% - needs to be clearly understood that
Top example – the IP address from Spain seen earlier – all coming back to different places in the same locality
Bottom example – IP address is assigned by British company BTInternet – and they move IP address around the country as demand requires. This example is from the slide author’s UK address in the north of England which was in Penrith, Cumbria. The returned information in the search is considerably out and wrong – but is the company offering the geolocation service’s best effort based on the information they have. The IP address has clearly been moved around to suit the business needs of British Telecommunications (BT)

## Slide 67
Finally
TRACERT to show DNS & data movement
The route the single packet took to get from the east coast of Spain to the west coast of Australia
Notes: The slide content is hidden behind the final graphic!
This graphic shows a tracert on a domain in Australia – completed from a Spanish IP address
Traceroute = network diagnostics for the real time path taken from source to destination
Firstly – uses DNS to decide what IP address CSU.EDU.AU is at
1 Need to find the default gateway (router) to get out – 192.168.18.1
2 Finds the ISP 45.14.248.1
3 Special internal IP address within comms network
4 Valencia (VLC02) hub of Cogentco.com – large multinational internet provider – Probably lease nolimitnet.eu internet lines
5 Madrid (MAD05) hub of Cogentco.com
6 Further hop within Cogentco.com – still in Madrid
7 Moves to NTT.COM in London (Londen uk) – global internet service
8 Further London hop
9 Crosses Atlantic to NTT.COM hub in Ashburn, Virginia (asbnva02)
10 Crosses USA to NTT.COM hub in San Jose, California (snjsca04)
11 Further hop in California
12 Further hop in California
13 Crosses Pacific to AARNET – high speed internet company in NSW, Australia (AARNET.NET.AU)
14 Further hop in AARNET
15 Further hop in AARNET
16/17 times out request (not unusual in Traceroute requests)
18 Hits IP address it set out to find at Charles Sturt University

## Slide 69: Internet services & applications
Computer & Internet Basics
Section 4

## Slide 70
Internet services
Notes: Before going into detail about the services available on the Internet, it is worth reflecting on how much countries now rely on those services at the national level. Trainers should provide an overview of the critical national infrastructure in their own countries to ensure that delegates understand how important the Internet has become in national infrastructure security issues in a short space of time.

## Slide 71
Internet services
What is on the Internet?
  WWW
  Email
  Peer 2 peer
  FTP
  Online Storage
  IOT – Internet of Things
  Online gaming
  Newsgroups
  Social networking
  IRC
  Instant Messenger
  VOIP – Voice over IP
  Deep web & Dark web
Notes: The Internet can be thought of as the infrastructure over which many different applications can be run simultaneously. If any part of the Internet malfunctions or is destroyed, communication can still continue. No-one owns the Internet – no organisation, no corporation, no government. It is largely self regulated. It all uses the same connection technology.
Most modern data networks, like the Internet, are described as “connectionless” or “packet switched”. Traffic is split into small packets which make their own way from sender to receiver. They do not all follow the same route and are joined together again when they reach their destination.
Most people connect to the Internet through an Internet Service Provider (ISP). These are commercial organisations that rent out space. They keep records…but for how long? There are national and international legal data protection or privacy issues that impact on how long data may be retained by ISPs. This of course has an impact on the ability of criminal justice officials to secure evidence from these sources. Connection is normally made by one of the following methods; Dial-up, Broadband (ADSL), ISDN, Cable, Wireless hotspot or Satellite.

## Slide 72
WWW
Since 1991, HTML (Hyper Text Markup Language) has allowed words, pictures & sound on web pages
Uses the HTTP protocol – Hyper-Text Transfer protocol
  Used by browsers & web servers to communicate using HTTP request & responses
Notes: The World Wide Web (WWW) was effectively born in 1991 when HTML – Hyper Text Markup Language was invented by Sir Tim Berners-Lee. HTML provided the platform to combine words, pictures and sounds on web pages. Web standards are created by World Wide Web Consortium (W3C). The following explanation goes someway to explaining the name.
“The W3 world view is of documents referring to each other by links. For its likeness to a spider's construction, this world is called the Web.” (Tim Berners-Lee, Robert Cailliau; World­Wide Web; Sept 1992

## Slide 73
WWW
Resources are found at URLs
  Uniform Resource Locators
http://www.coe.int
http = Process being used
www = World Wide Web server
coe = Domain name
int = Top level domain (often with country)
Notes: This slide to show the different parts of a URL – and how they combine to get to the end result

## Slide 74
WWW
Websites are a series of linked (and non linked) pages
To land here
  www.sitename.com
Other
.html
Services
.html
Contact
.html
About
.html
Services.html
Services.html
Services.html
Services.html
Index
.html
Home Page
To land here
  www.sitename.com/about.html
Notes: This slide to try to show the way a site is constructed from home page down through levels of linkage – and also how you can go to a specific page if you know the exact URL
Also means that if you knew About.html wasn’t linked in any way – but you know the correct URL for it, you could get to it – a ‘hidden page’

## Slide 75
WWW
Web page as seen in a browser
Source code which the browser interprets to display the web page
Notes: Each page is written in a code – called HTML (Hyper Text Markup Language)
Source code of any page can be viewed by right click on a clear part of the page
It is sometimes readable and understandable – but it’s main role is to tell a BROWSER what it should display – positioning, colour, content, where to get it from …….
Possible to hide things in HTML code – which is not displayed on screen but is ‘within’ the page – in the background

## Slide 76
WWW traces
Web servers retain logs of requests
  Time, date, IP address, location, pages visited, etc.
This is a graphic representation of a webserver log
The actual logs are highly textual & require work to understand then & provide evidence from them
Notes: Web logging will keep - Your identity (IP address) Date and time you accessed, What you looked at, How long you looked at it, how often you looked, Your browser, Your operating system, How you got to the page
Investigators need to be aware that this information is kept and can be used for evidence/intelligence or if it is an investigator visiting within an enquiry, can be used against them if they have not fulfilled legal obligations

## Slide 77
Email
Appearance that this goes direct between machines – it actually goes through a number of computers which can add/remove useful data
Internet
SMTP
Server
POP3
Server
SMTP
Server
Alice
Bob
ISP will add data
May add or remove data
POP3 Mail & IMAP Mail
Principle is similar
Notes: Electronic Mail or Email is a method of exchanging digital messages.
To the user, It appears that E-mail is passed directly from the sender's machine to the recipient's; however each message typically passes through at least four computers during its lifetime.
  A Message is composed on user’s own computer, then sent to ISP's outgoing SMTP mail server* (Simple Mail Transfer Protocol or SMTP)
  Outgoing ISP forwards e-mail onto recipient’s ISP SMTP mail server* (SMTP – SMTP)
  Recipient’s mail server finds recipient's incoming mail server (Post Office Protocol or POP3) and delivers message to ‘recipient’s post box’
  Recipient logs onto account and message is retrieved into recipient’s inbox, normally deleting it from the mail server in the process
* Mail server – dedicated computer used to handle mail
This graphic is massively simplified – to aid basic understanding of the process
E-mail - The traditional Outlook type mail – sent via SMTP – retrieved via POP3 and once downloaded resident on your own machine
Web-based mail - POP3 mail; for instance using Outlook – when you log in you normally download all new mail into you inbox resident on your machine; IMAP mail – ‘true’ web-mail – viewed via your machine but still resident on a remote server – can be organised into folders, etc. but only visible when online.

## Slide 78
Email
What’s in an email?
Short headers
Message body
Full headers
Notes: The graphics show the content of a mail recovered rom the author’s junk folder – which is a spam/fraudulent email.
A live known example from the trainer’s own mail may assist

## Slide 79
Email
Email investigative issues?
Headers exist in all emails – but no standard method to access them
  Clients or web-mail all have different locations
Some mail apps will remove headers
  Google (Gmail), Hotmail, Hushmail
  Done for ‘privacy’
Always read from ‘bottom upwards’
Notes: All emails will have headers – which provides some potential evidence of where the email originated from – in terms of an IP address. It can also provide some other ‘leakage’ such as a computer name
Although they exist, they can be difficult to get to – all email clients and web based mail have different ways to get to the headers. Best advice is to do some internet research to find out how
Some providers (Gmail, Hotmail) choose to strip header information such as IP addresses – for privacy purposes
When looking at an email header, the rule is to extract the header – then read it from the bottom upwards which is the order ‘data’ will have been added to it. Therefore the first IP address is likely to be the source.
Some emails are very straightforward – some are less so. And the analysis can be done manually or using some internet tools – which can also interpret the data incorrectly at times

## Slide 80
Email ‘dead letter box’
Applicable to web based email – hotmail, Gmail, Livemail, etc
Create email online – add attachments if required
Save as ‘Draft’ – don’t send it
Share account login details for others
  Never sent, deleted when message passed
Notes: Different ways in which criminals use the Internet services should be of interest to the participants. One such use is the “dead letter box”. This may be explained by the trainer as it is fairly easy to understand how this method of communication may be used with little risk of capture – nothing is actually sent between people – it is only accessed
Depending on the time and resources available, this exercise can be done by all participants or only be shown/explained by the trainer as a live demo

## Slide 81
P2P - Peer to Peer
Repository for legitimate file sharing – and also known for allowing illegal content & files subject to intellectual property/copyright
Centralised network replaced with de-centralised
  System of peers & supernodes/ultrapeers that facilitate the sharing
  Shareaza, Frostwire, e-mule
Notes: Peer to Peer services have for many years allowed the transfer of illegal files as well as files that are subject to intellectual property rights. Peer to peer clients have been popular among criminal groups involved in these activities. First generation peer-to-peer architecture worked on the principle of using a centralised server to which people connected in order to download files. This made identification of those offering illegal services fairly easy to locate and close down. Second generation peer to peer clients use different methods of connectivity from those that hold lists of available files to make searching easier to those that act as supernodes that identify where files are available.
Judges will need to be aware of peer to peer activity as it may be relevant to many types of criminal and civil trial. An in depth knowledge is not necessary and training designers should consider using sites such as http://ezinearticles.com/?How-Peer-to-Peer-(P2P)-Works&id=60126 to provide up to date information.

## Slide 82
P2P – Peer to Peer
Notes: This slide shows the interconnectivity of a peer to peer network – where through the individual Ultrapeers having all their peers connected, each then connects to another and the network geographically grows. Means that a file can be downloaded from almost any part of the network, once that connection is made and a search on it can take place

## Slide 83
P2P – Peer to Peer
Notes: The screenshot shows Shareaza – a peer to peer application. A search was completed for an audio file of the Abba song ‘Waterloo’ – the network found 436 instances of files that fitted the criteria – Build 1
We can then see the result returned to the computer is the file name, the file type (extension) and then the size of it. The rating is a network score where users have voted on the quality.
The status column shows how available the file is – three green ticks is the best result whilst a red X says the file is not presently downloadable. This could be due to the user going offline so the direct connection cannot be made.
Host count will show the IP address if it one IP address that is sharing this file – or the selection can be expanded to show multiple IP addresses sharing the same file. The exactness of the file is calculated by hashing the file within the network – Build 2
Double click the file and the download starts to the computer

## Slide 84
FTP – File Transfer Protocol
Allows file transfer – between computers
Works on client/server basis – with FTP program installed on the client
  Works with user ID & password
  Once credentials authenticated, TCP connection opened for transfer
  e.g. FileZilla, CuteFTP, File Downloader, CoreFTP
Notes: FTP is short for File Transfer Protocol. A protocol is a set of rules that networked computers use to talk to one another. And FTP is the language that computers on a TCP/IP network (such as the internet) use to transfer files to and from each other.

## Slide 85
FTP – File Transfer Protocol
Notes: The screenshots show the FTP clients FileZilla & CuteFTP – trainer can describe the way they act in a similar way to Windows File Explorer except instead of looking at local machine contents, they are looking at the contents of two different machines connected over the internet.
These pieces of software have vast functionality as can be seen from the drop down menus
Therefore they have a connection window showing the connection taking place and then the sending and receiving machines – along with the connection status of the transfers

## Slide 86
Online storage
Cloud computing is prevalent – storing data in the ‘Cloud’
Convenient, on-demand, shareable, safe
  Free – may be provided by your ISP or others
  Subscription – sign up, pay & get more storage
Legitimate
Criminally used
  They can store & share content
Notes: Cloud storage involves stashing data on hardware in a remote physical location, which can be accessed from any device via the internet. Clients send files to a data server maintained by a cloud provider instead of (or as well as) storing it on their own hard drives
At its heart, cloud computing involves using the power of the internet to outsource tasks you might traditionally perform on a personal computer – anything from handling simple storage to complex development and processing – to a vast and powerful remote network of interconnected machines.
This outsourcing is handy for the casual user who is fed up of having to free up space on their hard drive or purchase new storage for all the cat/baby/food photos they can’t stop taking. It’s even better for businesses that want to use the cloud for processing and storage – because users only pay for what they use.

## Slide 87
Online storage
Examples – iDrive (5GB/5TB), pCloud (10GB/2TB), OneDrive (5GB/6TB), Google Drive (15GB/2TB)
Mega.nz
15GB free
Max 16TB
Fully encrypted at server end & in transit
(128 bit AES)
Notes: Some examples of storage available August 2020 – figures in brackets are free capacity offering & max paid for capacity. Trainer needs to get the magnitude of what is now not on the machines we are investigating – but could be in the cloud
Also have to consider that there could be a synchronisation – where it could be in both places
Example is Mega.nz – where 15GB is free & 16TB is max capacity. The data is uploaded over a web browser – and then available to anyone logging in with username & password. Data is encrypted on the server – and the owner (Kim DotCom) will happily hand over the data to law enforcement – in its encrypted form. The encryption protocol that MEGA uses is the standard 128-bit AES encryption for your at-rest files, plus it encrypts your data while in transit using the TLS protocol, also with 128-bit AES. This means that your files are secure both while on the MEGA.nz servers and while being uploaded or downloaded, so your data is safe from man-in-the-middle attacks

## Slide 88
IOT – Internet of Things
Every device is connected with its own IP address (IPv6) – interconnected with owner & each other
Challenge – devices contain data & can become targets as impossible to secure everything
Compromised devices can be used as Botnet!
  e.g. Mirai
Notes: The Mirai Botnet:
The incident (December 2016) took offline some of the most popular sites on the web, including Netflix, Twitter, Spotify, Reddit, CNN, PayPal, Pinterest and Fox News – as well as newspapers including the Guardian, the New York Times and the Wall Street Journal.
The cause of the outage was a distributed denial of service (DDoS) attack, in which a network of computers infected with special malware, a “botnet”, are coordinated into bombarding a server with traffic until it collapses under the strain.
Unlike other botnets, which are typically made up of computers, the Mirai botnet was largely made up of so-called “internet of things” (IoT) devices such as digital cameras and DVR players.
Because it has so many internet-connected devices to choose from, attacks from Mirai could be much larger than what most DDoS attacks could previously achieve.
It was estimated that the attack had involved “100,000 malicious endpoints”, and there had been reports of an extraordinary attack strength of 1.2Tbps, roughly twice as powerful as any similar attack on record.

## Slide 89
Online gaming
Popular with some – who spend considerable amounts of time playing
Online communities formed of gamers
Cybercrime permeates gaming
Hacking - Cyber criminals try to lure you to give information about yourself so they can hack your personal or gaming accounts
Phishing - They may tell you they can help you get more game currency or level up faster
Gold-farming - Cyber criminals use botnets to generate in-game assets—such as “gold”, “coins”, or “gems” - sell to other players, typically at a discount.
Cyberbullying - Part of the fun in online gaming is the competitiveness between players. Difference between harmless competition and cyberbullying
Notes: An online game is a game played over some form of computer network. This almost always means the Internet or equivalent technology, but games have always used what technology was current; modems before the Internet and hard-wired terminals before modems.
The expansion of online gaming has reflected the overall expansion of computer networks from small local networks to the Internet and the growth of Internet access itself.
Online games can range from simple text-based games to games incorporating complex graphics and virtual worlds populated by many players simultaneously.
Many online games have associated online communities, making online games a from of social activity beyond single player games

## Slide 90
Online gaming
FIFA 2020
Sims 4
Call of Duty Black Ops 4
Notes: Games are FIFA 2020, The Sims 4 & Call of Duty (Black Ops 4)

## Slide 91
Newsgroups
Usenet = User’s Network – known as Newsgroups
Thousands of ‘bulletin boards’ or online discussion forums on differing subjects
  Available worldwide where almost anyone can post
Legitimate
Criminally used
  Share illegal materials
Google Groups (since 2001 when they bought Deja) – or commercially available services
Notes: The term Newsgroup is somewhat of a misleading description as they tend to host discussions. They are technically different but function in a similar way to discussion forums hosted on the World Wide Web. Newsgroup servers are hosted by various organisations who agree with others that they will synchronise their information on a regular basis. This allows users to post messages to one server and be seen by a larger audience.
Been around for many years – and although considered ‘old’ in internet terms, they are definitely still up and running – and catering for the sharing requirements of many

## Slide 92
Newsgroups
Notes: On the left is a listing of commercial newsgroups services available August 2020.
On the right is the website of Giganews – the build more interesting in the cybercrime world when they talk about the privacy, security, etc

## Slide 93
Social Networking
Communication & lifestyle choice of many
Facebook, Twitter, Instagram, TikTok, Snapchat, YouTube, Tumblr, Pinterest
Create profiles, gather friends, share information & data
  Issues with amount of data ‘shared’ which makes people target of criminals
  Useful resource for law enforcement gathering information about suspects & activities
Some are pure messengers – others have them!
Notes: Instant Messaging and Social Networking have taken over as the communications tool of choice in recent years with many well known examples providing instant and user friendly access to other users throughout the world.
The main feature of these sites is the ability to create a personal profile and share information about yourself and to meet new people. It is possible to share photos music and videos.
The amount of personal information that is posted by individuals can make them a target for criminals for example those involved in identity theft and those wishing to groom children.
Social Networking sites are a very useful vehicle for law enforcement to gather information about suspects and illegal activities
Instant messaging is a form of real time direct chat between two or more individuals using shared clients.
This type of chat involves contact between known person as opposed to other types of chat that allow communication between unknown persons. Criminals are known to use instant messaging as a method of communication.

## Slide 94
Social Networking
Notes: Trainer should take a short time to look at the impact of this graphic – and why social media is such an important area for crime & criminal investigation
The build emphasises usage & growth

## Slide 95
Social Networking
Notes: This highlights the changes in behaviours & technology – scenes from Rome and a papal inauguration
And it continues to increase with speeds & devices now connected to the Internet – and so social networks

## Slide 96
Social Networking
Here’s what we had for dinner today!
(look yesterday & day before for previous meals)
Guess where I am?
(time & date supplied)
Some things are actually quite funny!
This is the 8th day in a row that I’ve put a picture of my dog on Facebook!
People put things online to share with their friends, family …….. and the world!
Which provide opportunity for law enforcement if used correctly!
Notes: Typical things people put on line – which provides opportunity for law enforcement - if they have the authority to do so & can collect it properly – and it’s relevant

## Slide 97
IRC – Internet Relay Chat
Dated chat programme but still used in many criminal areas to communicate & exchange files
Series of servers worldwide – ‘channels’ created which are text based, virtual meeting rooms
  Channel names tend to reflect chat contents
  User can connect to one or more channels
  Not most user friendly – but effective
Notes: Internet Relay Chat (IRC) is in effect a teleconferencing system that is somewhat dated but still used by criminals to communicate and exchange files.
It works by a series of servers connecting to each other and sharing messages that are posted in “Channels”, which are text based, virtual meeting rooms.
The discussion topics are listed and users who have an IRC client may connect to one or more channels at any time to engage in discussion with likeminded people.
IRC is not the most user-friendly service on the Internet and is mostly used by those who are more experienced and potentially older users.

## Slide 98
IRC – Internet Relay Chat

## Slide 99
Instant Messenger
Communication used to be by cell/mobile phone calls
That was followed by chat clients & SMS
The trend continues with messenger services on both computers & mobiles with textual, pictorial and video capability
Move to encrypt communication too
Notes: Icons are messenger, WhatsApp & telegram
Trainer should be aware of what messengers are – and their ability to perform simple text messaging – moving through into the sending & receiving of images, sounds, files & video – and then to video calling – which appears on the next slide as VOIP

## Slide 100
VOIP – Voice over IP
Ability to conduct telephone-like calls over the internet – most likely encrypted
Creates real-time communication channel – at no cost apart from the hardware
First conceived in 1973 – became reality in 1996
Popular especially where internet speed is good
Notes: A natural extension of messengers but now being seen not just in business & corporate environments but also in the home world.
Zoom - a company no one had heard of before COVID – went from obscurity to fame overnight with the ability to connect people who couldn’t otherwise meet personally
Zoom is a video conferencing app, geared towards business usage. It was founded in 2011, by Eric Yuan, and launched in January 2013.
While gathering considerable popularity and coming to run profitably in the following years, Zoom truly entered the public consciousness during the coronavirus pandemic of 2020. It was to Zoom that users across the world turned to stay in touch during the lockdown effected to stop the spread of the virus.
Why ever people chose the app, Zoom usage shot up in March 2020. Yuan stated in a blog post that over the course of that month, Zoom was seeing 200 million daily meeting participants (not DAU). The following month, this figure had risen to 300 million. This compares to 10 million in December 2019

## Slide 101
VOIP – Voice over IP

## Slide 103: Deep web, anonymity & the dark web
Computer & Internet Basics
Section 5

## Slide 104
Deep Web
Graphics like this frequently are used to illustrate the part of the internet
The figures are estimates – but close enough!
Can search & link from page to page
Pages are unlinked & need exact URLs to reach –
or usernames & passwords with authentication
Need bespoke software to access
Notes: While the Internet is a place where service and information providers typically want to publish and share data with the general public, there is also a demand for more private areas accessible to a restricted group of people for exclusive purposes. Some of these areas are public places that can only be found by people who have the correct address. Take for example, the couple that want to share photographs of their wedding with their family and friends. They would not want every user of the Internet to see the photos. In this case they could upload the pictures to a cloud service and share the link to the gallery only with personal friends and family. Of course this is not a very secure way to share private data, but it is easy and since the photos would not be regarded as highly confidential this solution might be enough for most people.
There are also other hidden areas of the Internet for which login credentials are needed. A typical bulletin board and a normal webmail account are just two examples of private areas that cannot be found by a search engine or accessed because of their login requirement. Besides the sites that are intentionally hidden from public search engines, there are also websites and databases which cannot be indexed by the search engines because their contents cannot be understood or analysed by them.
The collective name for all those areas of the Interne that are hidden from search engines is called the “Deep Web” (other names are “Hidden Web”, “Invisible Web” or “Deepnet”).
Besides the websites, databases and documents that are not indexed by the search engines there is another layer of the Deep Web: the so-called “Darkweb”. The Dark Web, cannot be searched by the standard search engines. However, while Deep Web websites can be accessed by a normal web browser if the visitor knows the address or the login credentials this is not true for Dark Web websites.
The Dark Web is constituted from Dark nets that are small peer-to-peer networks, as well as large popular networks like Freenet, I2P and ToR.

## Slide 105
Anonymity
There are many anonymity resources available
Why?
  Some people have an urge to not be traceable
  They may be in fear of reprisal/identification
  May have been blocked & want a work-around
  They may be doing something illegal
Applications
Proxies & VPNs
TOR Browsers (or similar)

## Slide 106
Anonymity programmes/sites
Browser & mail anonymity programs
Notes: The highlighted website provide anonymity or encryption to protect the sender. Some are free – some have a paid service. They illustrate how simple it is to do things on the internet where tracing the suspect or offender is so difficult – due to them using technology to obfuscate.
They also offer facility to ensure nothing is left lying on a server which can be interrogated – whilst removing IP address information

## Slide 107
Proxy v VPN
Proxy acts as a ‘gateway’ to a web based resource
VPN creates a secure tunnel for all communication
Notes: A VPN is quite similar to a proxy. Your computer is configured to connect to another server, and it may be that your route web traffic through that server. But where a proxy server can only redirect web requests, a VPN connection is capable of routing and anonymising all of your network traffic
A virtual private network (VPN) extends a private network across a public network and enables users to send and receive data across shared or public networks as if their computing devices were directly connected to the private network. Applications running across a VPN may therefore benefit from the functionality, security, and management of the private network. Encryption is a common, although not an inherent, part of a VPN connection.[1]
A trainer demo may be the best way to describe how someone can move around the world – whilst sitting on a chair in front of the delegates

## Slide 108
VPN
Notes: Some examples of VPN – some are free – some are paid. The free ones tend to have paid versions which offer faster bandwidth & more upload/download capacities

## Slide 109
VPN
Legal
Secure
Locations
Speed
Notes: This slide shows a VPN – VPN Unlimited
Purpose is to illustrate the uses & configurability of a VPN – how it can be used to appear to be anywhere
Legal – yes in almost all places. They have legitimate uses – but also can be misused
Secure – Yes, the end to end encryption that is in place through the tunnel it creates gives security – which can be misused too – to avoid interception
Locations – most will have multiple locations throughout the world to appear to be somewhere else
Speed – using a VPN will slow your connection down a little as it has to encrypt the data it is sending – but with today’s high speed internet connections, it won’t be too bad

## Slide 110
Dark Web
Brief History
2000 – Freenet released
2002 – US Navy release TOR
2009 – Satoshi Nakamoto mines first Bitcoin
  (March 2009 = $0.003 – 17 December 2017 = $19,783)
2011 – Silk Road begins
2013 – FBI arrest Dread Pirate Roberts (Ross Ulbricht) – owner of Silk Road
2019 – Figures suggest $1bn trades
Notes: Another subject where a basic overview has to be done – and where we could spend days rather than a few slides. The builds here are followed by explanatory slides for most
Besides the websites, databases and documents that are not indexed by the search engines there is another layer of the Deep Web: the so-called “Darkweb”. The Dark Web, cannot be searched by the standard search engines. However, while Deep Web websites can be accessed by a normal web browser if the visitor knows the address or the login credentials this is not true for Dark Web websites.
The Dark Web is constituted from Dark nets that are small peer-to-peer networks, as well as large popular networks like Freenet, I2P and ToR.

## Slide 111
TOR
TOR – The Onion Router
c.65,000 unique URLs
  End with ‘.onion’
Many legal – many not!
  Privacy & protection
  Underground marketplaces
  Drugs, weapons, services, stolen identities, pornography, paedophilia
  Cryptocurrencies
Truth about the Dark Web – Kumar & Rosenbach
Notes: A trainer demonstration would be a useful addition to this slide to illustrate TOR and some services available – requires internet connection or pre-recorded TOR session

## Slide 112
TOR
Why is it called ‘the onion router’?
A
B
C
Notes: TOR is built on encryption – and the passing of encrypted information between nodes
Each node only knows where the previous node is and the following node – nothing about the origin or any further nodes – building up an encrypted route
Each communication (or tab in the browser) takes a different route – but each uses the same entry point – or guard node
Communication could be intercepted – but you would only intercept encrypted data
The original data is ‘wrapped’ with the encryption key of each node the data is going to pass through – and that layer is removed by the node as it passes on its way – the last hop is the only time data is unencrypted – or it would be unreadable

## Slide 113
Cryptocurrencies
Bitcoin history
2009 – Satoshi Nakamoto mines first Bitcoin
Notes: Trainer facilitates a discussion about cryptocurrencies
Icons – Bitcoin, Litecoin, Ethereum, Zcash, Dash, Ripple, Monero

## Slide 114
Cryptocurrencies
Characteristics of cryptocurrency
Global – no borders
Decentralised – no control
Volatile – can fluctuate wildly
Secure – ‘Private Key’
Anonymous
Created by mining
Transparent (Blockchain)
Low transaction fees
Fast transfer
Irreversible
No legal tender status
Retained in ‘wallet’
A medium of exchange
A unit of account
A store of value
Notes: Trainer facilitates a discussion about cryptocurrencies
Icons – Bitcoin, Litecoin, Ethereum, Zcash, Dash, Ripple, Monero
The points again show how cryptocurrency works – and how it can be used to deal with illegal purchases or money laundering
Widely acknowledged definitions of virtual currencies/digital currencies refer to the work done by the Financial Action Task Force (FATF), an inter-governmental body developing and promoting policies to combat money laundering and terrorist financing.
According to FATF, A virtual currency is a digital representation of value that can be digitally traded and functions as
1. a medium of exchange;
2. a unit of account; and/or(3) a store of value, but does not have legal tender status in any jurisdiction.
According to FATF, Digital currency can mean a digital representation of either virtual currency (non-fiat) or e-money (fiat). The term digital currency provides a term by which it is possible to refer to digital representations of both fiat and non-fiat currencies.
A crypto currency is a digital currency in which encryption techniques are used to regulate the generation of units of currency and verify the transfer of funds, operating independently of a central bank. Crypto currencies are a subset of alternative currencies, or specifically of digital currencies.
Definition given by the European Court of Justice: “49. Transactions involving non-traditional currencies, that is to say, currencies other than those that are legal tender in one or more
There are almost 6400 different crypto currencies (08/2020). A nice overview can be found here: http://coinmarketcap.com/all/views/all/
The by far most important and most well-known crypto currency is Bitcoin which was invented in late 2008 by „Satoshi Nakamoto“. However, it is important to know that there are also other crypto currencies as well. Some of them were created because Bitcoin became too „heavy“ – meaning that it is not really handy to pay transactions. Others were created to overcome weaknesses of Bitcoin, e.g. DASH (the X11 Logo; formerly known as Darkcoin) to allow fully anonymous transactions or Litecoin to allow faster transactions as well as smaller transactions.
Most of the currency are based on the same approach: A peer-to-peer network to mine coin and validate transactions and a pre-defined, limited supply of the currency.
Here are some explanations for vocabulary that is frequently used when talking about crypto currencies:
The Wallet: A wallet is loosely the equivalent of a physical wallet on a crypto currency network. The wallet actually contains the owner‘s private keys which allow him to spend coins allocated to his address in the block chain.
The Miner: Mining is the process of making computer hardware do mathematical calculations for the crypto currency network to confirm transactions.
The block chain: The block chain is a public record of all transactions in the network of the crypto currency. They are stored in chronological order. The block chain is shared between all users of that network and is used to verify the balance of wallet addresses.
The private key: The private key is a secret piece of data that proves your right to spend coins from a specific wallet address through a cryptographic signature. Each wallet address has its own unique private key.

## Slide 115
Marketplaces
Marketplace history
2011 – Silk Road begins
Market places come – and go!

## Slide 117
Session recap
After this session, delegates should be able to:
Recognise the common components of a digital device & understand their role
Describe what the internet is, how someone connects to it & what possible traces can be left in doing so
List some internet services & applications which may they may encounter in their role as prosecutors & judges
Give examples of issues the dark web could bring to criminal prosecution
Notes: This session is going to be split into 5 parts to provide natural breaks.
Idea is to describe what a computer is – or a device capable of connecting to the internet which all have similarities
The to describe what the internet is and how it works
And then to look at how that computer connects to the internet
And then look at what is out on the internet itself

## Slide 118
Thank you
Xxxxx XXXXXXXX
Council of Europe
email
DD Month YYYY
Introductory Judicial Training Course on Cybercrime and Electronic Evidence