## Slide 1: Session 10
Examination and analysis of Electronic Evidence

## Slide 2: Session Objectives
At the end of this session the participants will be able to…
Distinguish between traditional computer forensics and mobile forensics
Discuss options for the storage of digital evidence
Describe considerations for determinining the volatility
Outline procedures to collect log files
Summarise the evidential items which can be found digital devices
Summarise options for decrypting data
Discuss different documentation techniques
Identify methods for physical and logical extractions
Distinguish between different levels of examinations and analysis techniques
Describe techniques to analyse hidden data, application data and files
Identify methods to analyse e-mail evidence and network traces
Summarise the elements of a forensic report

## Slide 3
Digital Forensics
Computer Forensics
Mobile Forensics
Network Forensics
Post Mortem Forensics
Live Forensics
Application Forensics
Physical extraction & analysis
Logical extraction & analysis
Other devices: e.g. wearables
Live Network Forensics
Captured Packets Forensics
Malware Analysis
Multimedia Forensics
Embedded Forensics
IoT Forensics
Smart home Forensics
Automotive Forensics
Other Devices: e.g. gaming consoles
Physical
recovery
Notes: There are three main categories of Digital Forensics.
Computer Forensics is the oldest of the categories. It affects personal computers, servers and storage media. There are four subcategories of Computer Forensics. They are
Post Mortem Forensics, which is all about how to acquire, process, analyse and report data stored on computer systems that are not turned on. This is the most traditional category of forensic.
Physical recovery involves the physical disassembly of storage media which may be damaged or destroyed (e.g. exchange of disk heads, chip-off)
Live Forensics is all about how to acquire, process, analyse and report data stored on computer systems that are turned on. Compared to Post Mortem Forensics it is a rather young subcategory but is becoming more and more important as a lot a data nowadays is stored temporarly, remotely or encrypted.
Application forensics is the subcategory that focuses on analysing traces and artefacts left be thousands of different applications.
Multimedia forensics includes the extraction and analysis of data from CCTV and DVR systems as well as the in-depth analysis of video, audio and picture files (e.g. forgery)
The last category is the forensics pertaining other hardware devices, such as routers, game consoles, skimming devices and many more. A lot of these devices have their own propriotary file systems and operation systems.
The first three categories have subcategories for the different operation systems, like Windows, Linux, Mac OS X
Mobile Forensics is becoming more and more important, since a lot of data that can be interesting for an investigation can be stored on mobile devices like smartphones and tablet computers. The sub-categories include the physical and logical extraction. The physical extraction using bootloaders, firmware hacks, chip-off techniques and alike requires more in-depth knowledge and is rather time consuming, while the logical extraction typically just requires the examiner to extract data using mobile forensics software/hardware suits.
The category network forensics handles electronic evidence that is transmitted over a network, be it wireless or wired, be it Internet or a local area network. In live network forensics the investigators are facing a situation where they are intercepting a network connection and need to analyse the datastreams on-the-fly. While the captured packets forensics deals with analysing files that contain recorded network traffic.
The forensic analysis of embedded systems is getting more popular because more and more IoT and Smart home/garden/etc devices are being used. It also includes the very broad field of Automotive IT forensics.

## Slide 4: Storage of evidence
The original evidence should be stored in secure facilities as highlighted in Session 6.
access control
fire protection
temperature and humidity control
protection from magnetic sources
avoid static charges

## Slide 5: Storage of evidence
The same applies for the storage of
forensic images (typically ewf/E01):
access control
fire protection
temperature and humidity control
protection from magnetic sources
avoid static charges
redundant storage
Notes: A forensic laboratory needs to have a storage facility to store backups of the forensic copies/images. It is good practice to not only have one backup but also another off-site backup. While the digital forensic analyst is conducting the analysis with his working copy of the image there should still be a backup stored on another system (e.g. an imaging server).
Image: https://commons.wikimedia.org/wiki/File:Rack_Servers_Fujitsu_Primergy_2.jpg
Source: Own work
Author: Trique3030

## Slide 6: Computer vs. mobile forensics
Process model of computer forensics:
Process model of mobile forensics:

## Slide 7: A high-level comparison
Computer forensics: Mobile forensics:
Notebooks, Desktops, Servers - Mobile phones, tablets
Similar hardware setups - thousands of makes and models
Mostly Windows, Linux, macOS - Mostly Android, iOS
Typically more in-depth analysis - Typically more tool driven
Different options to image - Limited access to hardware

## Slide 8: Computer forensics

## Slide 9: Determination of volatility
2.1 Order of Volatility
When collecting evidence you should proceed from the volatile to the less volatile. Here is an example order of volatility for a typical system.
registers, cache
routing table, arp cache, process table, kernel statistics, memory
temporary file systems
disk
remote logging and monitoring data that is relevant to the system in question
physical configuration, network topology
archival media
Source: IETF – RCF 3227
Notes: https://www.ietf.org/rfc/rfc3227.txt

## Slide 10: Collection logs
List all actions together with dates, times and acting person
Help documenting all measures
Are important for the Chain of custody

## Slide 11: Decryption
Ways to tackle encryption:
Passwords stored digitally / analog
Weak passwords
Dictionary attacks
Extraction of keys from RAM
Notes: At this point, the video „forensic_analysis_ram_sneakpeak_voice_over.mp4“ could be shown.

## Slide 12: Documentation
All steps in the process of collecting, handling and analysing electronic evidence must be documented
Checklists, forms and audit logs help to complete the documentation
Notes: Picture is taken from Appendix I of the CoE „Digital Forensics
A BASIC GUIDE FOR THE MANAGEMENT AND PROCEDURES OF A DIGITAL FORENSICS LABORATORY „

## Slide 13: Physical & logical extraction
There are two types of copies:
Physical: includes all raw data, including unallocated subset of data
Logical: includes just allocated data
While the forensic examiner will always aim for the physical set of data, it is not always possible to obtain physical copies, e.g. encryption, no physical access, time constrains, etc
Notes: There are two types of copies; a physical and a logical one. While a physical copy includes all raw data, a logical copy typically only includes an allocated subset of all that data. On disk level for example a physical copy includes the whole disk including the partitioning scheme, all partitions and even unpartitioned areas while a logical copy on disk level is just a copy of one logical partition.
A digital forensic analyst should typically aim for a full physical copy of a whole disk because it includes deleted and formerly allocated areas. However, when dealing with encryption a logical copy of the unlocked data is preferred to a physical copy of the encrypted data. There can also be situations during a search and seizure operation where creating a physical copy might not be possible, out-of-scope or simply not covered by the warrant or other authority.
Both, the physical and the logical copy can be written in different ways. Either they are cloned, which means that the data is directly copied bit-by-bit from one storage medium to another, or they are written as an image file, which means that all data is copied bit-by-bit from one storage medium into one or more image files on a target medium. The latter technique is the more common one as writing the data into an image file offers some advantages like compression, error correction checksums, inclusion of meta data.

## Slide 14: Visualisation and examination aids
For aiding in visualisation of complex data structures, visualisation aids can be helpful. Examples for those aids are:
Timelines: Indicating the behaviour of the user: When did the suspect log in, when did he connect a certain medium, when did he connect to which wireless lan, when did he view which website, etc.
Relationship diagrams: Can give answers to the questions: Who has met whom at which point of time using which medium? Which information was sent/received? Who knows whom? Who is the main suspect who coordinated the others?
Communication diagrams: Similar to a relationshop diagram but does not necessarily involve persons. It could show how often which IP addresses attacked a server from which country.
Moneyflow diagrams: Can help to understand at which point of time which amount of money has been sent over which channel by which persons.
Notes: Graphical representations make it easier to understand the correlation between the data. They can also enable the investigator to find new links. Typically the basis for such diagrams are raw data which are stored in a structured way, e.g. csv/tsv files. Those files are loaded into specialised commercial or some free software. On Linux for example simple commands like awk, sort, uniq used in conjunction with Graphviz or dot can help drawing graphical representations.

## Slide 15: Temporal analysis
Can reveal:
Activities on certain dates/times
Corralations between events
Notes: The screenshots shows the timelining function of the open source tool „Autopsy“.
Picture source: https://www.sleuthkit.org/autopsy/images/v3/tl_counts.png
A good demonstration video can be found here: https://www.sleuthkit.org/autopsy/timeline.php

## Slide 16: Relational analysis
Can reveal:
Communication between individuals
Accounts used on different channels
Data/money/ asset flows
Notes: Picture source: https://sleuthkit.org/autopsy/docs/user-docs/4.7.0/communications_page.html

## Slide 17: Relational analysis
Can reveal:
Communication between individuals
Accounts used on different channels
Data/money/ asset flows
Notes: Picture source: https://sleuthkit.org/autopsy/docs/user-docs/4.7.0/communications_page.html

## Slide 18: Data hiding analysis
Renamed files (e.g. jpg disguised as txt)
Steganography:
Notes: Note: This slide is animated
Has anyone of you used magical ink when you were small kids? The concept is that you can hide text by writing it with the juice of a lemon. Althought your whole text is written on paper unencrypted it cannot be seen by someone who does not know that there is a message on the paper written with this magical ink. The person you are sending this paper to knows of course how to make your hidden message visible. Those of you who know the technique: Do you remember how to make the ink visible? [click] by carefully heating the paper using a candle or lighter

## Slide 19: Data hiding analysis
Another method of hiding the true content of a file/volume is encryption

## Slide 20: Application and file analysis
Each operating system (e.g. Windows, Linux, macOS) stores information about user preferences and user activity (e.g. log files, registry, historic backups, etc).
Each application typically stores its own preferences, user-settings, log files, cache, etc.
Each filesystem stores meta information about its files (e.g. last access, deleted date, ownership, attributes, etc).
Some files may store meta information (e.g. exif data incl. camera make, model, geo-locations, etc).

## Slide 21: Application and file analysis - Examples
Notes: It is a good idea to show the „Forensic_analysis_examination_2_voice_over.mp4“ and the „Forensic_analysis_registry_voice_over.mp4“ video.
Screenshot of a parsing for recently opened documents from a Windows registry and from the video „Forensic_analysis_examination_2_voice_over.mp4“.

## Slide 22: Email analysis
Can reveal:
Communication details
Attachements
Contacts details
Notes: Picture source: http://sleuthkit.org/autopsy/docs/user-docs/4.16.0/email_parser_page.html

## Slide 23: Email header analysis
Can reveal:
Transport flow of the message
Originating IP address
Originating mail server / service provier
Notes: This is the e-mail header found in the suspect‘s mail account.

## Slide 24: Can reveal: Which IP address communicated with which other address. The actual contents transferred.
Network analysis
Notes: Picture source:
https://commons.wikimedia.org/wiki/File:Wireshark_Example_Decode.png
The picture shows the network analysis tool „Wireshark“ highlighting a network packet capture showing network packet requesting DNS information for en.wikipedia.org.

## Slide 25: Preparation of report
Notes: Pictures are taken from Chapter 6.4. of the CoE Standard Operating Procedures for the collection, analysis and presentation of electronic evidence

## Slide 26
Notes: Pictures are taken from Appendix J of the CoE „Digital Forensics
A BASIC GUIDE FOR THE MANAGEMENT AND PROCEDURES OF A DIGITAL FORENSICS LABORATORY „

## Slide 27: Mobile forensics

## Slide 28
Notes: It is estimated that 80% of the world’s population (3.5 billion people) have a smartphones.
We use them all day, everyday. For work and for pleasure. They can hold so much valuable evidence.

## Slide 29: What can we hope to find?
Pictures and videos.
Text messages.
Photo messages (multi-messaging service)
Call logs (received, dialled, missed)
Contacts.
Emails (depending on device)
Internet history.
Social media.

## Slide 30: Unique Identification
IMEI – International Mobile Equipment Identity
IMEI is a unique number for identifying a device on a mobile network.
You can think of it as your phone’s social security number. It has 15 digits and is assigned to most phones
123456789012345
Notes: The IMEI number must be recorded when conducting a phone examination. Phone cases can be removed thereofore serial numbers may also be erased. The only sure way to confirm that the device is the same is by the IMEI number.

## Slide 31
*#06#
Notes: Open your phone and dial *#06# - this will give you the IMEI number of your phone.
If your phone is lost or stolen your phone network provider can use this number to trace your phone or to remotely lock it.

## Slide 32: Challenges
Competitive market – always creating new devices
Notes: Trainer – Please upload pictures of the latest devices new to market – to emphasise the point that mobile technology is always changing. Forensic software providers are constantly playing ‘catch up’ to new technology. So forensic examination of new devices may not be supported by current software/extraction methods.

## Slide 33: Encryption
Mobile device manufacturers are very secretive about their product.
Many social media offerings are encrypted
Criminals desire more security
Pass codes, Biometrics
Notes: Manufacturers take steps to protect their operating systems – so that competitors cannot steal their ideas – making it more difficult to navigate around devices and apps and capture electronic evidence.
Increasing development of social media apps offering ‘end to end encryption’.
Criminals are seeking more ways to communicate secretly – talk about the latest EncroChat Police take over. 2020

## Slide 34: Examples….
'EncroChat' smartphone system used by the mafia to move money, drugs and order murders.
EncroChat was a secret platform where users were able to communicate privately between specially-designed handsets - often to run drugs, traffic people and even order murders. Feb 2020
Notes: https://papernewsnetwork.com/police-roll-up-crime-networks-in-europe-after-infiltrating-popular-encrypted-chat-app-techcrunch/
Sometimes the Police get lucky!

## Slide 35: Social media Applications
Offering end to end encryption:
Signal
WhatsApp
Telegram
Threema
Etc.
Notes: Pictures sources:
https://commons.wikimedia.org/wiki/File:Threema%27s_App_Icon.png
https://commons.wikimedia.org/wiki/File:Signal-logo.png
https://commons.wikimedia.org/wiki/File:WhatsApp.svg
https://commons.wikimedia.org/wiki/File:Facebook_Messenger_logo_2020.svg
https://commons.wikimedia.org/wiki/File:Telegram_2019_Logo.svg

## Slide 36: Examination of Mobile Devices
7 levels
Depending on the circumstances and the device
Activity must be recorded camera/video
Activity must be recorded contemporaneously.
A third party must be able to follow examiners actions and arrive at the same conclusions
Notes: The seven levels are:
Simple (basic) manual extraction
Logical extraction
File System capture
Physical extraction
J-Tag, Hex Dump
Chip Off
Micro Read.

## Slide 37: Different levels of examination
Manual
Logical
File System
Physical
JTAG/Hex Dump
Chip Off
Micro Read (highly sophisticated)

## Slide 38: Manual Extraction
Examiner browses the phone in real-time and takes a photograph of any valuable data.
Does not recover deleted
Time consuming
Notes: Basic level phone forensics – recording information from the mobile phone screen while utilizing user interface. As the examiner is interacting directly with the phone – data will be changed so contemporaneous notes are valuable the examiner’s actions should be recorded.

## Slide 39: Logical Extraction
Notes: A logical extraction is the equivalent of asking a mobile device “what data would you like to give me?”. It recovers live and accessible data from most native applications, such as Messages and telephone calls. On Android devices, it does not typically recover data from third party applications such as WhatsApp, Facebook Messenger, however this data is often extracted during a logical of an iPhone. This requires the device to be powered on and often requires changes to the device’s settings to allow for a successful connection. This is the quickest type of extraction, and can be used to quickly get access to live data or to quickly triage a device

## Slide 40: FSD Extraction
File System Extraction
Slower than a logical Extraction
Can recover some deleted data
Recovery of third party applications from Android
Notes: A file system (FSD) extraction is a middle ground between a logical and a physical examination, but still often considered a logical extraction (of sorts). It recovers live and limited deleted data and has more chance of recovering third party application such as WhatsApp and Facebook Messenger from Android devices. The file system examination reads all the files that are stored within the mobile device’s file system and copies them out for the forensic software to interpret. Sometimes within these files, depending on the file type, deleted entries may still be stored and therefore recoverable. This requires the device to be powered on and often requires changes to the device’s settings to allow for a successful connection. This is the equivalent of asking the device “please just give me a little bit more data?”

## Slide 41: Physical Extraction
Recovery of deleted data
Can be time consuming
Device may remain off
Notes: A physical extraction is where a bit-by-bit copy of the data storage is taken from the device, giving the best chance for recovery of all available live and still recoverable deleted data. Depending on the make and model of the device, this can sometimes be done without powering the device’s Operating System on as the extraction method can take advantage of recovery partitions and vulnerabilities in the device’s start up procedure. Alternatively, if the device is required to be powered on, some changes to the settings will be required and the device may need to be “rooted” (where a user is given elevated user privileges) to allow for access to protected system areas. This is the equivalent of a “smash and grab” - the device has no choice but to give you all data. This can take a significant period of time, anywhere from an hour to several hours, depending on the storage capacity of the device.

## Slide 42: JTAG Extraction
Labour intensive
Time consuming
High level of technical ability required
Notes: JTAG stands for Joint Test Action Group, and was mainly used for device manufacturers to debug their devices before launching them. JTAG is a non-invasive form of physical acquisition that could extract data from a mobile device even when data was difficult to access through software avenues because the device is damaged, locked or encrypted. The device, however, must be at least partially functional (minor damages would not hinder this method).
labour-intensive, time-consuming procedure, and it requires advance knowledge (not only of JTAG for the model of the phone under investigation but also of how to interrogate the resulting binary composed of the phone’s memory structures).
Physically soldering connections from the phone’s JTAG pins to access the flash memory of the device.

## Slide 43: Chip Off Forensics
Invasive
Required high level of technical skill and knowledge
Renders the device unusable
Easy to lose data
Time consuming
Expensive
Notes: A process that refers to obtaining data straight from the mobile device’s memory chip.
The chip is detached from the device and a chip reader or a second phone is used to extract data stored on the device under investigation.
It should be noted that this method is technically challenging because of the wide variety of chip types existing on the mobile market. Also, the chip-off process is expensive, training is required, and the examiner should procure specific hardware to conduct de-soldering and heating of the memory chip.
Bits and bytes of raw information retrieved from the memory are to be parsed, decoded, and interpreted. Even the smallest mistake may lead to damages to the memory chip, which, in effect, would render the data irrevocably lost.

## Slide 44: Preparation of Report
Scope
Contents
Organisation

## Slide 45
Notes: Here we are using Cellebrite as an example of mobile device examination. Once the phone has been downloaded – we are provided with this detailed homepage providing links to all the available analyzed data.

## Slide 46
Notes: After examination of the data we can prepare a report which will contain the required evidence.

## Slide 47: Session Review
At the end of this session the participants will be able to…
Distinguish between traditional computer forensics and mobile forensics
Discuss options for the storage of digital evidence
Describe considerations for determinining the volatility
Outline procedures to collect log files
Summarise the evidential items which can be found digital devices
Summarise options for decrypting data
Discuss different documentation techniques
Identify methods for physical and logical extractions
Distinguish between different levels of examinations and analysis techniques
Describe techniques to analyse hidden data, application data and files
Identify methods to analyse e-mail evidence and network traces
Summarise the elements of a forensic report

## Slide 48: Questions?